## Slide 1: WF on low-PAPR/CM technique
3GPP TSG RAN WG1 Meeting #86 R1-168367
Gothenburg, Sweden 22nd - 26th August 2016
Agenda Item: 8.1.2.1
Ericsson, DoCoMo, Huawei, Nokia, Panasonic, Qualcomm, Vodafone, OPPO

## Slide 2: Background
Already agreed: At least up to 40 GHz for eMBB and URLLC services, NR supports CP-OFDM based waveform …, possibly with additional low PAPR/CM technique(s) (e.g., DFT-S-OFDM, etc.)
Unclear:
  Would possible “additional low PAPR/CM techniques” be for DL+UL or UL only?
  Would possible “additional low PAPR/CM techniques” be complementary or always used?
  If complementary, would there be a common reference-signal/control-signal structure or different reference-signal/control-signal structures

## Slide 3: Proposal
Already agreed: At least up to 40 GHz for eMBB and URLLC services, NR supports CP-OFDM based waveform …, possibly with additional low PAPR/CM technique(s) (e.g., DFT-S-OFDM, etc.)
Proposal:
  For data transmission, additional low-PAPR/CM technique(s) is only considered for uplink
    Additional low-PAPR/CM technique(s ) for special downlink signals such as sync signals is FFS
  Additional low PAPR/CM technique(s) is considered as complement to CP-OFDM without low-PAPR/CM technique(s)
  RAN1 should strive for maximum commonality, in terms of uplink reference-signal and control channel for CP-OFDM with and without additional low-PAPR/CM technique(s) if additional low-PAPR/CM technique(s) is to be supported.