## Slide 1: WF on PSBCH demodulation for V2V communication
Intel
3GPP TSG RAN WG1 Meeting #86 R1-168381
Gothenburg, Sweden, 22nd - 26th August 2016
Agenda item - 7.2.2.1

## Slide 2: Background
Demodulation performance of PSBCH is sensitive to the number of punctured symbols and number of available symbols [R1-166256, R1-166510]
Currently agreed physical structure and content size leads to very poor BLER performance due to puncturing of series of bits and consequent systematic error
RAN1 needs to address the issue and make it independent from DMRS allocation or punctured symbols

## Slide 3: Proposal
PSBCH rate matching is done across DMRS, PSSS, SSSS, the first, and the last symbols of PSBCH subframe