## Slide 1: WF on PUCCH retuning for BL/CE UE
Ericsson
R1-168461
AI 7.1.5
3GPP TSG RAN WG1 Meeting #86
Gothenburg, Sweden, 22nd 26th August 2016

## Slide 2: Background
Issues with the currently specified way to create guard periods for BL/CE UEs during PUCCH retuning through rate matching were discussed in the following contributions:
  R1-166498 On timeline issues with shortened PUCCH format Qualcomm
  R1-166630 Simulation results for PUCCH frequency retuning NEC
  R1-166684 PUCCH Structure for Frequency Retuning Samsung
  R1-167848 PUCCH frequency retuning for BL/CE UE Ericsson

## Slide 3: Proposal
Agree to specify the following UE behaviour (which is the same as the behaviour that was specified before RAN1#84):
  For PUCCH 1/1a/1b, UL retuning gaps are generated by puncturing of the affected SC-FDMA symbols: last symbol and first symbol of the prior and the latter subframe respectively
    However, if the prior subframe is an SRS subframe, shortened format of legacy behaviour is applied, i.e., shortened format is applied in the prior subframe, and first symbol of the latter subframe is punctured.
Ask RAN2/RAN to introduce a UE capability (or FGI bit) for the following, currently specified UE behaviour (which was introduced at RAN1#84):
  Shortening of PUCCH 1/1a/1b in the first slot of a subframe is realized by using in the first slot with PUCCH 1/1a/1b resource mapping from symbols 1 through 6 in the first slot while maintaining the existing PUCCH 1/1a/1b DM-RS locations.