## Slide 1
3GPP TSG RAN WG1 Meeting #86 R1-168498 Gothenburg, Sweden, 22nd - 26th Aug 2016
Agenda item: 8.1.5
WF on RS for CSI measurement in NR
Huawei, HiSilicon

## Slide 2: Background
Following WF has been agreed in RAN1#85:
  In NR multi-antenna schemes, studies on RS design and CSI acquisition considering following use cases
    Non-UE-specific RS use case for CSI measurement
    UE-specific RS use case for CSI measurement
      Note: functionally may be analogous e.g.: to R13/14 UE-specific beamformed CSI-RS (with dynamic beamforming)
      Note: maybe relevant to UE receiving beam sweeping
    Use of a joint operation among multiple RS from the same or different use cases
    RS for interference measurement use cases
    RS for channel reciprocity use cases
    Other use cases is not precluded
  Note: including measurement over aperiodic/periodic/semi-persistent RS
  Note: Subband RS is not precluded

## Slide 3: Proposal
At least following RS configurations for CSI acquisition are supported in NR
  Aperiodic RS
  Semi-persistent RS,
  FFS: periodic RS
Study RS design for CSI measurement in NR at least include
  RSs are mapped on one or a few symbols
    E.g., in a few consecutive symbols
  RS is located at the earlier part of a subframe
  FFS: RS located at other part of a subframe
Study on configurable density of RS in frequency domain
Note: Multi-level RS design can be considered
  E.g. functionally analogous to R13/14 hybrid non-precoded/beamformed CSI-RS and beamformed CSI-RS