## Slide 1: Way forward on time-domain structure
NTT DOCOMO, INC.
3GPP TSG RAN WG1 meeting #86 R1-168534
Gothenburg, Sweden
22nd – 26th August 2016
Agenda item: 8.1.3
Document for decision

## Slide 2: Background
Followings are considered as starting points of NR frame structure at least within the CP overhead
  Subframe
    Already agreed upon
    Assume x=14 in the reference numerology for subframe definition (for normal CP)
    FFS: y=x and/or y=x/2 and/or y is signalled
  Slot
    Slot of duration y OFDM symbols in the numerology used for transmission
    An integer number of slots fit within one subframe duration (at least for subcarrier spacing is larger than or equal the reference numerology)
    The structure allows for ctrl at the beginning only
    The structure allows for ctrl at the end only
    The structure allows for ctrl at the end and at the beginning
    Other structure is not precluded
    One possible scheduling unit
  Mini-slot
    Should at least support transmission shorter than y OFDM symbols in the numerology used for transmission
    May contain ctrl at the beginning and/or ctrl at the end
    The smallest mini-slot is the smallest possible scheduling unit (FFS: smallest number of symbols)
  Note: the names are for the purpose of discussion. Whether some terms can be merged or not is FFS
  FFS whether NR frame structure needs to support both slot and mini-slot or these can be merged

## Slide 3: Proposal (1)
On top of the agreement, how scheduling is done is further crystallized

## Slide 4: Proposal (2)
RAN1 considers followings as a starting point to study the frame structure
  Confirm that NR enables at least following in the case of 15 kHz subcarrier spacing as a reference numerology for subframe duration and 30 kHz subcarrier spacing for scheduling unit:
Subframe duration
Scheduling unit (DL-only, UL-only, and DL + UL)
Scheduling unit (DL-only, UL-only, and DL + UL)
Scheduling unit (DL-only, UL-only, and DL + UL)

## Slide 5: Proposal (3)
At least following are discussed until RAN1#86b:
  Relationship b/w scheduling unit and slot/mini-slot
  Channel/RS structure of each scheduling unit
  Whether/how to achieve scheduling unit shorter than x/2 symbols of the given reference numerology in a subframe duration is realized
For each proposed time-domain structure, companies are encouraged to clarify use-cases
  E.g., carrier frequency, SCS, eMBB/URLLC, etc