## Slide 1: WF on Path Loss Calibration for mMTC
Qualcomm Incorporated, Mediatek
3GPP TSG RAN WG1 #86 R1-168543
Gothenburg, Sweden, 22nd- 26th August 2016
Agenda item: 8.1.7

## Slide 2: Background
In RAN1 #85 the following simulation SLS assumption is agreed for mMTC
Attributes | Values or assumptions
Layout | Single layer - Macro layer: Hex. Grid
Inter-BS distance | 1732m
Carrier frequency | 700MHz
Simulation bandwidth | Companies report simulation bandwidth used in evaluation
Channel model | 3D UMa Take 5GCM output into account if applicable.
Tx power | UE: Max 23dBm or optional 10dBm
BS antenna configuration | Rx: 2 and 4 ports (8 as optional)
BS antenna pattern | Follow the modelling of TR36.873
BS antenna height | 25m
BS antenna tilt | Companies report tilt
BS antenna element gain + connector loss | 8 dBi, including 3dB cable loss
BS receiver noise figure | 5 dB
UE antenna elements | 1Tx
UE antenna height | 1.5m
UE antenna gain | -4dBi
Traffic model | Non-full buffer small packet. Consider future trend of mMTC traffic
UE distribution | 20% of users are outdoor in cars (100km/h) or 20% of users are outdoors (3km/h) 80% of users are indoor (3km/h) Users dropped uniformly in entire cell
BS receiver | MMSE-IRC as baseline, Advanced receiver is not precluded
UL power control | Companies report power control scheme
Channel estimation | Realistic

## Slide 3: Proposal
Pathloss calibration between companies to ensure path loss tail match NBIoT
If needed to introduce additional penetration loss to ensure path loss tail match NBIoT