## Slide 1: WF on SLS observations of non-orthogonal MA
Huawei, HiSilicon, ZTE
3GPP TSG RAN WG1 #86bis R1-1610793
Lisbon, Portugal, Oct 10 - 14, 2016
Agenda item: 8.1.1.2

## Slide 2: Background
Significant efforts on extensive UL LLS and SLS evaluation have been devoted with great many contributions comparing the performance between non-orthogonal MA and OFDMA under agreed parameters

## Slide 3: Observation
Based on system-level simulation results and assumptions summarized in [R1-1610531], it is observed that
  All simulated non-orthogonal MA schemes with grant-free provides significant system capacity gain (summarized in Appendix 1) in terms of packets arrivals rate (packets/s/sector) @ given system outage (e.g, 1% target packet drop rate), compared to a reference scheme based on OFDMA with grant-free
  Evaluation simulators have been calibrated with agreed simulation assumptions (R1-1609442)
R1-1610531, “Summary of preliminary SLS results”, Huawei, HiSilicon, Lisbon, Portugal 10th - 14th October 2016.
R1-1609442, “Summary of email discussion thread 86-15 and 86-17 on SLS calibration for NR MA”, Huawei, HiSilicon, Lisbon, Portugal 10th - 14th October 2016.

## Slide 4: Proposal
Capture the observations on page 3 and slides 5-6 into TR 38.802
  Slides 5-6 are to be updated based on updated simulation results submitted to this meeting

## Slide 5: Appendix 1: preliminary SLS results (1/2)
 | Huawei | QC | ZTE | CATT | Samsung | CATR
MA | SCMA (R1-1608854) | RSMA (R1-1610120) | MUSA (R1-1608952) | PDMA (R1-1608756) | IGMA (R1-1609042) | SCMA (R1-1609581)
Inter-BS distance | 1732m | 1732m | 1732m | 1732m | 1732m | 1732m
Simulation bandwidth | 6 PRB | 1.08MHz | 6 PRB | 4 PRB | 6PRB | 4 PRB
BS antenna tilt | 2 degress | 6 degress | No Mechanical downtilt | 12 degree | 6 degress | 100 degree
BS antenna element gain + connector loss | 8 dBi, including 3dB cable loss | 8 dBi, including 3dB cable loss | 8 dBi, including 3dB cable loss | 8 dBi, including 3dB cable loss | 8 dBi, including 3dB cable loss | 8 dBi, including 3dB cable loss
UE antenna gain | -4dBi | -4dBi | -4dBi | -4dBi | -4dBi | -4dBi
UL power control | P0= -90dBm, alpha=0.9 | P0 = -126.4dBm ,Alpha = 1 | Po = -100 dBm, alpha = 1 | P0=-95dBm and alpha = 1 | P0=-90 dBm, alpha=1 | OFDMA: alpha=1, P0= -90 dBm SCMA: alpha = 1, P0=-95dBm
Channel estimation | ideal, realistic | ideal | ideal | ideal | ideal, realistic | ideal
Packet size | Fixed to 40 bytes as TBS, and baseline OFDMA is segmented to 2 packets | Follow TR45.820, TBS of 200 bit is used to segment the packet | Fixed 40 bytes, with segmentation to 2 packets | Fixed 40 bytes, with segmentation to 2 packets for ODFMA and PDMA. | Fixed by 40 bytes, segmentation not known | Fixed by 20 bytes
Packet dropping timer | 1s | 10s | 1s | _ | 1s or 10s | _
HARQ/Repetition | Maximum repetition/retransmissions of 32 | HARQ till packet dropping timer to mimic the TTI bundling. | HARQ until the fixed dropping timer. | Maximal number of HARQ transmissions is 16. | HARQ until the fixed dropping timer | No repetition or retransmission
OFDMA PAR at target PDR (Packets/ms/sector) | 0.6 (@PDR = 1%) | _ | 0.18 (@PDR = 1%) | 0.6 (@PDR = 1%) | 0.052 (@PDR = 1%, 1s drpping timer) | 0.1 (@PDR = 1%)
NoMA PAR at target PDR (Packets/ms/sector) | 2.1 (@PDR = 1%) | 0.68 (@PDR = 1%) | without secondary spreading: 2, with secondary spreading: 8 (@PDR = 1%) | PDMA:1.8 (@PDR = 1%) | 0.116 (@PDR = 1%, 1s drpping timer) 0.43 (@PDR = 10%, 1s drpping timer) | 0.2 (@PDR = 1%)
Gain over baseline grant-free OFDMA | 350% | _ | without secondary spreading: 1100%, with secondary spreading: 4400% | 300% | 830% @PDR 10% | 200% (@PDR = 1%) 250% (@PDR = 10%)

## Slide 6: Appendix 1: preliminary SLS results (2/2)
 | Intel | ETRI | Docomo | MTK | Nokia (R1-1609651)
MA | LCRS (R1-1609498) | LSSA (R1-1609549) | NOMA (R1-1610077) | RDMA(R1-1609334) GOCA(R1-1609335) | NOCA (R1-1609651)
Inter-BS distance | 1732m | 1732m | 1732m | 1732m | ISD=500m
Simulation bandwidth | 6PRB | 6RB | 6PRB | 6PRB | 72 PRBs
BS antenna tilt | _ | 102 degree | No Mechanical downtilt | 96 degree | _
BS antenna element gain + connector loss | 8 dBi, including 3dB cable loss | 8 dBi, including 3dB cable loss | 8 dBi, including 3dB cable loss | 8 dBi, including 3dB cable loss | 8 dBi, including 3dB cable loss
UE antenna gain | -4dBi | -4dBi | -4dBi | -4dBi | -4dBi
UL power control | fixed target SNR = 0 dB? | Alpha=1, P0= -90 dBm | _ | Alpha = 1, P0 = -95dBm | Alpha = 0.8, P0 = -80dBm
Channel estimation | ideal | ideal | ideal, realistic | ideal | ideal
Packet size | 20 bytes | 20 bytes | 20~200 Bytes based on TR45.820; Fixed packet size 40 Bytes (segmentation unknown) | Fixed 40 Bytes, segmented into 2 20Bytes RLC PDUs. | 100bytes by using 72 PRB
Packet dropping timer | 40ms | _ | 1s and 10s | 1 s | _
HARQ/Repetition | No HARQ for comparison results | No retransmission | HARQ/no HARQ random back-off | HARQ until the fixed dropping timer. | Max number of HARQ transmission: 1
OFDMA PAR at target PDR (Packets/ms/sector) | 0.5 @PDR 30% | Can not achieve proper PDR for analysis | _ | PDR floor at 2.5% | OFDMA:1.2 (PDR@ 10%)
NoMA PAR at target PDR (Packets/ms/sector) | 2 @30% | Can not achieve proper PDR for analysis | 0.1 (@PDR = 1%, 1s drpping timer) 0.25 (@PDR = 1%, 10s drpping timer) | RDMA:0.7 GOCA: 0.75 (PDR@ 1%) | NOCA: 6.2 (PDR@ 10%)
Gain over baseline grant-free OFDMA | 400% | Non-orthogonal scheme is more efficient than baseline OFDMA for PAR higher than 2.5. | _ | RDMA: 215% GOCA: 218% (@PDR 10%) | 516% @PDR 10%