## Slide 1: WF on SRS transmission
CATT, Nokia, ASB
3GPP TSG RAN WG1 Meeting #86bis R1-1611046
Lisbon, Portugal, October 10th - 14th 2016
Agenda Item: 8.1.4.4

## Slide 2: Proposals
NR supports subband SRS transmission
  Subband size can be configured
    Suband size can be equal to system bandwidth
  Frequency hopping can be supported for subband transmission
NR supports aperiodic SRS transmission
NR supports at least one of followings
  Periodic SRS transmission
  semi-persistent SRS transmission
Network triggered SRS transmission is supported
NR supports multiple numerologies for SRS transmission from one UE