## Slide 1: WF on collision handling in NB-IoT SC-PTM
Huawei, HiSilicon
R1-1613345
3GPP TSG RAN WG1 Meeting #87
Reno, Nevada, November 14-18, 2016
Agenda item 6.2.9.2

## Slide 2: Background
For NB-IoT SC-PTM, RAN1 has agreed:
  UE is not required to simultaneously monitor Type1-MSS and Type2-MSS
  UE is not required to monitor Type2-MSS while receiving NPDSCH carrying SC-MTCH
For NB-IOT SC-PTM, RAN2 has agreed:
  Reception of multi-cast in RRC_IDLE mode is required by both NB-IoT and MTC.
  Reception of multi-cast in RRC_CONNECTED mode is not required for NB-IoT and FFS for MTC.
  We consider to make the following agreement (working assumption for now):
    MT (paging) vs. SC-PTM: MT (Paging) has higher priority than SC-PTM
    MO (except signalling) vs SC-PTM: UE implementation
    MO signalling vs SC-PTM: MO signalling has priority.
RAN1 needs to define collision handling behavior on UE when collision happens between SC-PTM and paging/RACH;

## Slide 3: Proposals 1
Collision between SC-PTM related transmissions and NPSS/NSSS, NPBCH, and SIBs, is handled in the same way as unicast traffic in Rel-13 NB-IoT.
UE is not required to monitor Type1-MSS while receiving NPDSCH carrying SC-MCCH;
When a UE is monitoring NPDCCH search space for SC-MCCH or receiving NPDSCH carrying SC-MCCH, it is not required to simultaneously monitor NPDCCH search space for SC-MTCH or receive NPDSCH carrying SC-MTCH.

## Slide 4: Proposals 2
NB-IoT UE is not required to monitor NPDCCH search space of SC-MCCH or receive NPDSCHs carrying SC-MCCH when the UE is monitoring its Type1-CSS on paging occasions or receiving NPDSCHs carrying paging if paging has higher priority than SC-PTM.
NB-IoT UE is not required to monitor NPDCCH search space of SC-MTCH or receive NPDSCHs carrying SC-MTCH when the UE is monitoring its Type1-CSS on paging occasions or receiving NPDSCHs carrying paging message if paging has higher priority than SC-PTM.
  FFS: whether paging indicator in DCI format scheduling SC-MTCH is used to minimize unnecessary paging readings, e.g. in the case of neither paging message is scheduled nor direct indication is sent through the collided type1-CSS search spaces;
NB-IoT UE is not required to monitor NPDCCH search space or receive NPDSCH for SC-PTM when UE is receiving/sending messages during a RACH procedure.