## Slide 1
WF on System Information Delivery
LG Electronics, NTT DOCOMO, Inter Digital, [Qualcomm, SONY,]
R1-1613572
3GPP TSG RAN1 #87
Reno, USA, 14th – 18th Nov. 2016
Agenda Item: 7.1.2.2

## Slide 2: Background
NR defines at least one broadcast channel: NR-PBCH
  NR-PBCH decoding is based on the fixed relationship with NR-PSS and/or NR-SSS resource position irrespective of duplex mode and beam operation type at least within a given frequency range and CP overhead
    FFS: Unlicensed spectrum case
  FFS relationship between NR-PBCH subcarrier spacing and NR-PSS and/or SSS subcarrier spacing
  Following broadcasting schemes to carry essential system information can be considered
    Option 1: NR-PBCH carries a part of essential system information for initial access including information necessary for UE to receive channel carrying remaining essential system information
    Option 2: NR-PBCH carries minimum information necessary for UE to perform initial UL transmission (not limited to NR-PRACH) in addition to information in Option 1
    Option 3: NR-PBCH carries all essential system information for initial access
    Other options are not precluded

## Slide 3: Proposal
The system information other than those included in NR-PBCH is carried to the UE in the following options:
  Alt. 1: NR defines the additional channel as secondary broadcast channel
    Secondary broadcast channel may be different design from NR-PBCH, e.g. payload size, resource mapping, and etc.
  Alt. 2: The remaining information is transmitted in shared downlink channel similar to ,e.g. NR-PDSCH
  FFS : whether UE-specific, beam-specific and/or cell-specific
    Note: This does not preclude defining of other mechanisms transmitting system information, e.g. UE-specific/beam-specific for on-demand beamformed SIB and cell-specific otherwise.