## Slide 1
3GPP TSG RAN WG1 Meeting #88 R1-170xxxx
Athens, Greece, 13th – 17th January 2017
Agenda item: 8.1.1.1.2
WF on SS burst set composition
Huawei, HiSilicon, ZTE, ZTE Microelectronics, ITL, Motorola Mobility, Lenovo, NTT DoCoMo, [Intel], InterDigital, Sequans, …

## Slide 2: Background
In RAN1 NR AH meeting, the following agreements on SS structure were achieved:
UE shall be able to identify at least OFDM symbol index, slot index in a radio frame and radio frame number from an SS block
  The signals included in the SS block are FFS between
    Alt 1: PSS, SSS and PBCH; and
    Alt 2: PSS, SSS, TSS and PBCH
The time index/indices of an SS block from which UE will derive symbol, slot index in a radio frame is/are to be down-selected from the following alternatives:
  Alt 1: One time index for every SS-block within an SS-burst set
  Alt 2: One time index that is specific to each SS-block within an SS-burst, and an SS burst index that is specific to each SS burst within an SS-burst set. SS burst index is common across SS blocks in each SS-burst.
By default, the UE may neither assume the gNB transmits the same number of physical beam(s), nor the same physical beam(s) across different SS-blocks within an SS burst set.
UE may assume that a given SS block is repeated with a SS burst set periodicity
  Note that NR-PBCH contents in a given repeated SS block may change
A single set of possible SS block time locations is specified per frequency band.
  FFS whether the set is defined with respect to SS burst set or radio frame
  FFS whether idle/connected UE can be configured with additional information about which SS blocks in a SS burst set are transmitted

## Slide 3: Proposal
For SS burst set composition, NR defines one composition of SS block from the following candidates
  Alt 1:
    Each SS block consists of [4, 7] consecutive OFDM symbols
    SS blocks are not mapped across a slot boundary
    SS block is not mapped to first [1] OFDM symbol and last [1] OFDM symbol in a slot
    Note: There can be a gap of symbols between in the consecutive subframes/slots for example for UL and DL control symbols
  Alt 2:
    Each SS block consists of [4] consecutive OFDM symbols
    One SS block can be mapped across slots
    SS block is not mapped to first [1] OFDM symbol and last [1] OFDM symbol within a set of slots
  Alt 3:
    Each SS block consists of [3] distributed OFDM symbols
    Each SS block is mapped across consecutive slots
    SS block is not mapped to first [1] OFDM symbol and last [1] OFDM symbol in a slot
  Alt 4:
    One or more SS blocks can be transmitted within an SS block transmission window
    Each SS block consists of 3 (PSS/SSS/TSCH) or 4 (PSS/SSS/TSCH/PBCH) consecutive OFDM symbols, and is only mapped into one slot
      Note: Tertiary synchronization channel (TSCH) is used to indicate time location of the SS block within the SS block transmission window
      PBCH locations are predefined
  Note: slots described in the alternatives above are based on default numerology of the NR-SS

## Slide 4: Proposal
The maximum number of SS-blocks within a SS burst set may be carrier frequency dependent
  For frequency range category#1 (e.g., 4GHz), the number (L) is TBD within [1] ≤ L ≤ [8]
  For frequency range category#2 (e.g., 30GHz), the number is TBD within [10] ≤ L ≤ [64]
  FFS: L for additional frequency range category

## Slide 5: Examples of SS block mapping
Alt1:
  Each SS block consists on [4] consecutive OFDM symbols
  SS blocks are not mapped across a slot boundary
  SS block is not mapped to first [1] OFDM symbol and last [1] OFDM symbol in a slot

## Slide 6: Examples of SS block mapping
Alt2:
  Each SS block consists on [4] consecutive OFDM symbols
  One SS block can be mapped across slots
  SS block is not mapped to first [1] OFDM symbol and last [1] OFDM symbol within a set of slots

## Slide 7: Examples
Alt.3
  Each SS block consists of 3 non-consecutive OFDM symbols with fixed interval of a slot duration
  Each SS block is not mapped to first [2] OFDM symbols and last [2] OFDM symbols in each slot

## Slide 8: Examples
Alt. 4
  One or more SS blocks can be transmitted within an SS block transmission window
  Each SS block consists of 3 (PSS/SSS/TSCH) or 4 (PSS/SSS/TSCH/PBCH) consecutive OFDM symbols, and is only mapped into one slot
    Note: Tertiary synchronization channel (TSCH) is used to indicate time location of the SS block within the SS block transmission window
    PBCH locations are predefined