## Slide 1: [draft] Way forward on evaluation scenarios of physical layer SR in NB-IoT
Ericsson,[….]
R1-1706332
3GPP TSG RAN WG1 Meeting #88bis
Spokane, USA, April 3 - 7, 2017
Agenda item 7.2.6.1.2

## Slide 2: Background
In RAN#75, Further NB-IoT enhancements WI is introduced (see RP-170852).
Introducing SR is part of the WID as follows.
    Further latency and power consumption reduction
      Support for physical layer SR [RAN1, RAN2]
By adding support for a physical layer scheduling request (SR) the intention is to achieve further latency and power reduction in NB-IoT Rel-15.

## Slide 3: Background
In RAN1#88bis, a number of contributions provided argument on signaling design for physical layer SR in NB-IoT. However, the use case and impact on legacy NB-IoT system when introducing a new SR was not properly discussed.
Introducing dedicated SR in Rel15 would fragment the UL resource, and cause unnecessary DL overhead due to the scheduling of fragmented UL resource.
Appending SR with a HARQ ACK/NACK was studied in Rel-13 NB-IoT. But since Rel-13 NB-IoT system targeted short-lived traffic, the benefit of such a design was not pursued due to lacking of justifications.

## Slide 4: Proposals
SR should only be used when an NB-IoT UE is in uplink sync in RRC connected mode.
  TA estimation should not be a design target of SR signal.
The traffic model in TR 45.820 Annex E.2 is used for evaluating the justification of introducing dedicated SR.
  Baseline [30%] Network command, [70%] Mobile Autonomous Reporting.
The configuration of SR should be reported.
Latency evaluation can be based on the methodology given in Section 5.3 in TR 45.820 and the corresponding SR configuration should be reported.
The impact of DL and UL capacity of introducing SR should be reported.

## Slide 5: Proposals
If link level simulation is needed, the assumptions refer to the following table
Channel model | TU
Doppler spread | 1 Hz
Antenna configuration | 1Tx, 2Rx
Frequency error | ±50 Hz
Frequency drift | ±22.5 Hz/s
Distance between UE and eNB | 100km
UE transmit power | 23 dBm
MCL | 164 dB
SR resource configuration | Clarify when submit simulation results