## Slide 1: WF on Highest Code Rates Supported by LDPC
Ericsson, Fujitsu, Intel, LG, Qualcomm
R1-1709274
3GPP TSG RAN WG1 Meeting #89
Hangzhou, China, 15th – 19th May 2017
Agenda item 7.1.4.1.1.3

## Slide 2: Background (1)
Agreement (RAN1#87 Nov 2016)
In parity check matrix design, the highest code rate (Rmax,j ) to design j-th H matrix for is
  Rmax,j <=8/9
  Rmax,j is the code rate of the j-th H matrix before code extension is applied (0 j< J)
  Rmax,j is the code rate after accounting for the built-in puncturing, if this is applied in H matrix design
Rate matching to support transmission code rate higher than Rmax,j is not precluded

## Slide 3: Background(2)
In LTE, the highest code rate included in the MCS table is
In LTE, the UE is expected to be able to decode up to max code rate of 0.930
  TS 36.213: “The UE may skip decoding a transport block in an initial transmission if the effective channel code rate is higher than 0.931, where the effective channel code rate is defined as the number of downlink information bits (including CRC bits) divided by the number of physical channel bits on PDSCH.”
Cell-center UEs with good channel conditions can benefit from rates larger than 8/9.

## Slide 4: Proposal
In NR, the highest supported effective code rate for DL and UL transport blocks is at least as high as in LTE, i.e.