## Slide 1: WF on Physical layer SR
ZTE, Nubia
3GPP TSG RAN WG1 Meeting
Hangzhou, China 15th- 19th May 2017
Agenda item 6.2.7.1.2
R1-1709368

## Slide 2: Background
Solution options proposed in RAN1 #89 meeting to support SR sending with HARQ ACK/NACK:
Option1: QPSK (R1-1707022, R1-1707094, R1-1707572, R1-1707921)
Option 2: 900 rotation of BPSK-mapped ACK/NACK data symbols (R1-1708803)
Option 3: cover code/orthogonal sequence (R1-1707022, R1-1707572, R1-1707921)
Option 4: tone selection (R1-1707572)
Option 5: reserving two consecutive resources (one for ACK/NA CK, the other for SR) (R1-1707921)
It is observed that Option 4 and Option 5 need more time/ frequency resources and may need additional signaling overhead.

## Slide 3: Proposal
  Support piggybacked SR with HARQ-ACK for UEs with DL traffic from the following options:
    Option1: QPSK
    Option 2: 900 rotation of BPSK-mapped ACK/NACK data symbols
    Option 3: Cover code/Orthogonal sequence
  Dedicated SR is supported at least for UEs in good coverage.
    Periodic SR resources are configured by RRC signalling.
    FFS: Dynamic physical layer signaling to enable/disable the RRC configured SR resources