## Slide 1: WF on beam indication for PDSCH
Samsung, …
R1-1709382
3GPP TSG RAN WG1 Meeting #89
Hangzhou, China, 15 – 19 May 2017
Agenda item 7.1.2.2.1

## Slide 2: Background: RAN1#88 agreements
For reception of unicast DL data channel, support indication of spatial QCL assumption between DL RS antenna port(s) and DMRS antenna port(s) of DL data channel: Information indicating the RS antenna port(s) is indicated via DCI (downlink grants)
  The information indicates the RS antenna port(s) which is QCL-ed with DMRS antenna port(s)
    FFS: Indication details
      E.g. explicit indication of RS port/resource ID, or implicitly derived
  FFS when the indication is applied (e.g., the indication is assumed only for the scheduled PDSCH or until next indication; when the above information is included, if there should be a scheduling/beam switch offset, etc.)
  FFS: Beam indication for receiving fall back unicast PDSCH (if supported)
  Note: related signalling is UE-specific
FFS: Beam indication (if needed) for receiving (UE-group) common PDSCH for RRC connected UE
Candidate signalling methods for beam indication for a NR-PDCCH (i.e. configuration method to monitor NR-PDCCH)
  MAC CE signalling
  RRC signalling
  DCI signalling
  Spec-transparent and/or implicit method
  Combination of the above

## Slide 3: Background: RAN1#88bis agreement
For reception of DL data channel, study further at least the following:
  Whether or not have an effective window of spatial QCL assumption
  Interaction between higher layer signaling (if supported) and DCI indication
    FFS the signaling details for higher layer and DCI based approaches (e.g., the corresponding information field in DCI, etc.)
  Interaction between beam management and PDSCH transmission
  Whether or not to have a default behavior (e.g., due to DCI miss detection), and if so the default behavior
  Beam switching time, DCI decoding time, etc.

## Slide 4: Proposals
For reception of unicast DL data channel, the default QCL-ed DL RS antenna ports are those QCL-ed with the corresponding NR PDCCH for downlink assignment
  The default QCL-ed DL RS antenna port is applied when indication of QCL assumption between DL RS antenna port(s) and DMRS antenna port(s) of DL data channel is not configured in the DCI for downlink assignment