## Slide 1: WF on measurement based on CSI-RS for L3 mobility
NTT DOCOMO
3GPP TSG RAN WG1 Meeting #89 R1-1709413
Hangzhou, China
15th – 19th May, 2017
Agenda item: 7.1.1.5.2
Document for decision

## Slide 2: Background
At the last RAN1 meeting, following conclusions are made for mobility.
  Following remaining issues need to be finalized in the next meeting
    Properties of CSI-RS for RRM measurement for L3 mobility, e.g.,
      Timing of CSI-RS for RRM measurement for L3 mobility
      Bandwidth of CSI-RS for RRM measurement for L3 mobility
      Numerology of CSI-RS for RRM measurement for L3 mobility
      The number of REs in the freq. domain of CSI-RS for RRM measurement for L3 mobility
      Resource mapping and parameters of CSI-RS for RRM measurement for L3 mobility
      Configuration of CSI-RS parameters for RRM measurement for L3 mobility

## Slide 3: Proposal
Following CSI-RS properties for RRM measurement for L3 mobility are supported in NR
  Periodic CSI-RS transmission with configurable periodicity
    Note that CSI-RS transmission can be turned on and off
    FFS: candidate periodicity values
  Configurable transmission/measurement bandwidth
  Configurable numerology
  A certain association with SS block
    FFS : details on association, e.g., QCL between antenna ports and/or timing synchronization, and whether it is signaled to UE

## Slide 4: Offline outcome
Following CSI-RS properties for RRM measurement for L3 mobility are supported in NR
  Periodic CSI-RS transmission with configurable periodicity
    Note that CSI-RS transmission can be turned on and off
    FFS: candidate periodicity values
  Configurable transmission/measurement bandwidth
    FFS: whether/how transmission and/or measurement bandwidth is indicated to UE
  Configurable CSI-RS time/frequency resource
    Note that this property is the same with that for beam management based on CSI-RS
    Note that the numerology for CSI-RS should consider neighbor cell measurement aspects