## Slide 1: WF on the impact of power saving signal on paging reliability in MTC
Ericsson, Intel, Sony,
R1-1709470
3GPP TSG RAN WG1 Meeting #89
Hangzhou, China, May 15-19, 2017
Agenda item 6.2.7.1.1

## Slide 2: Background
The following agreements were made regarding physical signals to enable power saving at the NB-IoT UEs.
  A physical signal/channel indicating whether the UE needs to decode subsequent physical channel(s) is introduced, at least for idle mode paging. Candidates for the signal/channel are:
    Wake-up signal or DTX
    Go-to-sleep signal or DTX
    Wake-up signal with no DTX
    Downlink control information
    FFS whether synchronization to the camped-on cell is assumed for detecting/decoding WUS/GTS, depending on the (e)DRX cycle length
    Design details are FFS
  Connected mode DRX is FFS

## Slide 3: Back ground
Miss detection of, e.g., wake-up signal causes the UE missing paging.
False detection of, e.g., go-to-sleep signal causes the UE missing paging.
It is not desirable from the network point of view, the reachability of the UE is reduced due to the introduction of the pre-cursor signals.

## Slide 4: Proposals
The impact of physical signal/channel, on Idle mode paging reliability should be carefully studied and reported with the physical signal/channel design.
The reliability of the current paging mechanism can be used as the baseline.