## Slide 1: WF on UL Codebook Structure
Nokia, Nokia Shanghai Bell, CATT, Interdigital, …
3GPP TSG RAN WG1 Meeting #89
Hangzhou, P.R. China 15th – 19th May 2017
Agenda item: 7.1.2.1.3
R1-1709492

## Slide 2: Background
Agreements in RAN1 #88 meeting
In NR, support UE to report its capability regarding the max number of spatial layers (N) for UL transmission
NR supports UL codebook for an UE based on the reported capability, at least one of the followings is supported
  Alt1: Network configures multiple codebooks each corresponding to a # of antenna ports
  Alt2: Network configures a scalable/nested codebook supporting a variable # of antenna ports
  Alt3: Network configures a codebook same as UE capability
  Alt 4: UE recommends a subset of codebook(s)
    This alternative may be absorbed into one or more the above alternatives
  FFS the codebooks corresponding to a given number of TX antenna ports can be fixed in specification or configurable
UL codebook structure: at least one of the following two is supported
  Alt 0: single-stage codebook
  Alt 1: dual-stage codebook
Consider using LTE codebooks, the impact of multi-panel, etc. for UL codebook design

## Slide 3: Proposal
UL single-stage or dual-stage codebook support is a UE capability.
If single-stage codebook is supported, the codebook selection is based on gNB wideband and/or subband indication.
If dual-stage codebook is supported, the codebook structure is based on W=W1*W2 structure
  At least the selection of W1 is based on wideband indication from gNB.
    FFS partial-band indication of W1.
  The selection of W2 can be based on wideband indication or subband indication.