## Slide 1: WF on NR-RACH preamble format for high speed case
ZTE
3GPP TSG RAN WG1 Ad Hoc Meeting
HangZhou, China 15th – 19th March 2017
Agenda: 7.1.1.4.1
R1-1709573

## Slide 2: Requirements for high speed case
UE speed: 500km/h
Carrier frequency: Up to 6GHz
TRP and UE clock accuracy: 0.05 ppm at TRP, 0.1 ppm at UE
Cell radius: Up to 5km

## Slide 3: Proposal on premble formats for L = 839 and high speed case
Format | L | SCS(kHz) | BW (MHz) | N_OS | N_RP | T_SEQ (Ts) | T_CP (Ts) | T_GP (Ts) | Use case
3-A (1ms) | 839 | 5 | 4.32 | 4 | 1 | 4*6144 | 3168 | 2976 | High speed case
3-B (1ms) | 839 | 2.5 | 2.16 | 2 | 1 | 2*12288 | 3168 | 2976 | High speed case
Note:
L is the sequence lenght
Ts = 1/(30720) ms
Make down selection between 3-A and 3-B
FFS: Using restricted set (e.g LTE restricted set A, B)