## Slide 1
WF on Group Common PDCCH
Qualcomm, Ericsson
3GPP TSG RAN WG1 #89
Hangzhou, P.R. China, 15th – 19th May 2017
Agenda: 7.1.3.1.5
R1-1709582

## Slide 2: Backgrounds
Agreements:
NR supports a ‘group common PDCCH’ carrying information of e.g. the slot structure.
  If the UE does not receive the ‘group common PDCCH’ the UE should be able to receive at least PDCCH in a slot, at least if the gNB did not transmit the ‘group common PDCCH’.
  The network will inform through RRC signalling the UE whether to decode the ‘group common PDCCH’ or not
  Common does not necessarily imply common per cell.
  Continue the discussion on the detailed content of the ‘group common PDCCH’ including usage for TDD and FDD
  The term ‘group common PDCCH’ refers to a channel (either a PDCCH or a separately designed channel) that carries information intended for the group of UEs.
Agreements:
The staring position of downlink data in a slot can be explicitly and dynamically indicated to the UE.
  FFS: signaled in the UE-specific DCI and/or a ‘group-common PDCCH’
  FFS: how and with what granularity the unused control resource set(s) can be used for data

## Slide 3: Backgrounds
Agreements:
The UE will have the possibility to determine whether some blind decodings can be skipped based on information on a ‘group common PDCCH’ (if present).
FFS: if the data starting position is signaled on the group common PDCCH, the UE may exploit this information to skip some blind decodings
FFS: if the end of the control resource set is signaled on the ‘group common PDCCH’, the UE may exploit this information to skip some blind decodings
FFS: how to handle the case when there is no ‘group common PDCCH’ in a slot
When monitoring for a PDCCH, the UE should be able to process a detected PDCCH irrespective of whether the ‘group common PDCCH’ is received or not
Agreements:
‘Slot format related information’
  Information from which the UE can derive at least which symbols in a slot that are ‘DL’, ‘UL’ (for Rel-15), and ‘other’, respectively
  FFS: if ‘other’ can be subdivided into ‘blank’, ‘sidelink’, etc
FFS: ‘Control resource set duration’
  FFS: Indicates the duration of the control resource set(s)
  FFS: Can help the UE skip some of the semi-statically configured blind decodings. If not received, the UE performs all blind decodings.

## Slide 4: Proposal1
In ‘Slot format related information’, ‘other’ is divided into
  ‘Empty’
    Not used by gNB either for DL or UL
  ‘Reserved’
    UE shall not assume any for the symbol with ‘Reserved’, i.e.,
      UE cannot assume the transmission from gNB
      UE cannot assume UE can transmit
Group Common PDCCH can provide ‘Slot format related information’ for current slot and also future slots
  Max number of slots are FFS
  It is up to NW whether to provide ‘Slot format related information’ for current slot only or including future slots
Group Common PDCCH include reserved bits for future use
  Number of reserved bits is FFS

## Slide 5: Proposal2
Control resource set duration is not conveyed in Group Common PDCCH
Data starting position is not conveyed in Group Common PDCCH
  Data starting position is indicated by UE-specific DCI