## Slide 1: WF on QCL
Nokia, ASB, …
3GPP TSG RAN WG1 Meeting #89
Hangzhou, P.R.China, 15th - 19th May, 2017
Agenda: 7.1.2.4.5
R1-1709636

## Slide 2: Background (existing agreements)
Parameters for antenna port QCL in NR includes at least (if QCL is supported)
  Average gain, average delay, delay spread, Doppler shift and Doppler spread (same as in LTE)
QCL is defined as follows:
  Two antenna ports are said to be quasi co-located if properties of the channel over which a symbol on one antenna port is conveyed can be inferred from the channel over which a symbol on the other antenna port is conveyed.
Spatial parameter(s) for QCL in NR describes the spatial channel properties of the RS antenna ports observed at the receiver.
FFS: Spatial parameter(s) in NR also describes the spatial channel properties of the antenna ports at transmitter(s).
UE can assume same precoding for a DM-RS port and a PT-RS port
  Among which ports and mapping rules (fixed and/or configurable, etc) are FFS

## Slide 3: Proposal
Working assumption:
  RAN1 considers a generic term “spatial UE-Rx parameters” and defers to RAN4 performance testing the exact interpretation of “spatial UE-Rx parameters”.
  The following interpretation alternatives for “spatial UE-Rx parameters” can be further considered:
    One or more of: AoA, Dominant AoA, average AoA, Power Angular Spectrum (PAS) of AoA, average AoD, PAS of AoD, transmit/receive channel correlation, transmit/receive beamforming, spatial channel correlation etc.

## Slide 4: Proposal
Working assumption:
For CSI-RS RSRP determination, CSI-RS RSRP is measured per CSI-RS port.
Proposal:
DMRS ports in a DMRS group per [bundled PRB] in CC are implicitly assumed QCLed w.r.t average gain, delay spread, Doppler spread, Doppler shift, and average delay parameters, spatial UE-Rx parameters).
PTRS port and DMRS port are assumed QCL
  w.r.t average gain, delay spread, Doppler spread, Doppler shift, and average delay parameters, spatial UE-Rx parameters (e.g. PTRS and DMRS sharing the same beam)
  w.r.t Doppler spread, Doppler shift (e.g. PTRS and DMRS sharing the same RF chain)
CSI-RS ports within a CSI-RS resource have at least two types of QCL assumptions
  QCL w.r.t average gain, delay spread, Doppler spread, Doppler shift, and average delay parameters, spatial UE-Rx parameters
  Not QCL’ed (e.g. for beam selection based on beamformed CSI-RS codebook)

## Slide 5: Proposal
NR supports QCL indication across carriers, the default assumption being QCL assumptions per CC w.r.t average gain, delay spread, Doppler spread, Doppler shift, and average delay parameters, spatial UE-Rx parameters