## Slide 1: WF on LOS channel models for UMa AV and RMa AV
Ericsson
R1-1709650
3GPP TSG RAN WG1 Meeting #89
Hangzhou, China, 15th – 19th May 2017
Agenda item 6.2.8.1

## Slide 2: Background
A fruitful offline discussion was held

## Slide 3: Proposals on UMa AV LOS channel model
For UMa AV LOS pathloss
  For aerial UE height below 22.5m, reuse the same UMa LOS pathloss in TR38.901
  For aerial UE height between 22.5m and [150]m
    Reuse the PL1 formula from UMa TR38.901
    Note: since the height dependency of pathloss exponent based on current contributions is weak in UMa, the existing model for PL1 is adopted
    Further investigation into height dependency of pathloss exponent is encouraged
    Max applicability range in 2D distance is 4km
For UMa AV LOS shadowing
  Below 22.5m, 4dB, which is the same UMa LOS shadowing in TR38.901
  Between 22.5m and [150]m, shadowing with sigma_SF = A*exp(-B*h_UT)
    A and B are determined such that when sigma_SF = 4dB at h_UT =22.5m, and sigma_SF=1.5dB at h_UT=150m

## Slide 4: Proposals on RMa AV LOS channel model
For RMa AV LOS pathloss
  For aerial UE height below 10m, reuse the same RMa LOS pathloss in TR38.901
  For UMa AV LOS, for aerial UE height between 10m and [150]m
    Average proposals from multiple companies and obtain averaged pathloss for RMa LOS. Perform curve fitting on averaged pathloss taking breaking point into account