## Slide 1: Way Forward on bandwidth part for efficient wideband operation in NR
Ericsson, …
R1-17xxxxx
3GPP TSG-RAN WG1 #89
Hangzhou, China, 15th – 19th May 2017
Agenda item 7.1.7

## Slide 2: Proposals
Configuration of a DL bandwidth part includes at least one CORESET.
In case of one active DL BWP for a given time instant,
  A UE can assume that PDSCH and corresponding PDCCH (PDCCH carrying scheduling assignment for the PDSCH) are transmitted within the same BWP if PDSCH transmission starts no later than K symbols after the end of the PDCCH transmission.
  In case of PDSCH transmission starting more than K symbols after the end of the corresponding PDCCH, PDCCH and PDSCH may be transmitted in different BWPs
  FFS: Value of K (may depend on numerology, possibly reported UE retuning time, etc)
For the indication of active DL/UL bandwidth part(s) to a UE, the following options are considered (including combinations thereof)
  Option #1: DCI (explicitly and/or implicitly)
  Option #2: MAC CE
  Option #3: Time pattern (e.g. DRX like)
  Details FFS