## Slide 1: WF on DM-RS for Broadcast PDSCH
Qualcomm, Ericsson, LGE, Interdigital, ZTE, [Samsung, NTT DOCOMO]
3GPP TSG RAN WG1 Meeting #90 21st – 25th August 2017
Prague, Czech Republic
Agenda item: 6.1.2.3.3
R1-1714663

## Slide 2: Background
For broadcast/multicast PDSCH (other than PBCH), the PDSCH is transmitted with a single DMRS port:
  Support using only one front-load DMRS Configuration from Configuration 1 and Configuration 2. To down-select from:
    Alt 1: Configuration 1 (FFS 1 or 2 symbols)
    Alt 2: Configuration 2 with 2 symbols
  Support additional DM-RS. To down-select from:
    Alt 1: Additional DMRS is always present
    Alt 2: Additional DMRS is configurable
    FFS the number of additional DMRS symbol(s)

## Slide 3: Proposal 1
For broadcast/multicast PDSCH (other than PBCH), the PDSCH is transmitted with a single DMRS port:
  Support Alt 1: Front-load DMRS Configuration 1 with 1 symbol
  FFS: number and location of additional DMRS