## Slide 1: WF on RAN3 signaling support for LTE-NR coexistence feature
AT&T, CATT, Deutsche Telekom, Ericsson, Huawei, HiSilicon, Intel, Orange, Nokia, NSB, Samsung, T-Mobile USA, VIVO, Vodafone
3GPP TSG RAN WG1 Meeting #90 R1-1714892
Prague, Czech Republic, 21th – 25th August 2017
Agenda Item: 6.1.6

## Slide 2: Background
Agreements:
NR supports transmissions scheduled in LTE non-MBSFN subframes
  Mini-slots can be scheduled on OFDM symbols not carrying CRS
It is expected that NR scheduling and at least semi-statically reserved resources for forward compatibility can be used to avoid NR transmissions colliding with other LTE signals/channels (e.g., LTE PBCH/PSS/SSS, SIB1, LTE PDCCH region, etc.)

## Slide 3: Background
Agreements:
For LTE-NR coexistence in overlapping spectrum, support on the Xn interface and enhanced X2 interface messages
  FFS details, e.g., SCell ON/OFF, LTE MBSFN subframe configuration, synchronization aspects between LTE and NR, indication of semi-statically reserved resources in frequency domain, Indication of semi-statically reserved resources in time domain, etc.
For LTE-NR coexistence in adjacent spectrum, support on the Xn interface and enhanced X2 interface messages
  FFS details, e.g., synchronization aspects between LTE and NR, TDD UL/DL configuration, etc.
  FFS the case of multi-operator scenarios
Aim to conclude the FFS parts for the above and send an LS to RAN3 in the next meeting

## Slide 4: Proposal 1
For LTE-NR coexistence in overlapping spectrum,
  Send an LS to RAN3 to specify the Xn interface and enhanced X2 interface messages that enable coordination between LTE and NR, including
    LTE cell on/off configuration
    LTE MBSFN subframe configuration
    DL and/or UL carrier center frequency (ARFCN)
    Carrier bandwidth
    Signaling related to timing synchronization and SFN
      Note: this does not mean the network is synchronized
      Note: It is up to RAN3 if this requires new procedures in addition to signaling support
    Indication of semi-statically used resources (to avoid collisions with, e.g., CSI-RS, SRS, PRACH, PUCCH, DRS, PSS/SSS, PBCH, …)
    Indication of slots/PRBs not intended for transmissions by the eNB and gNB, respectively

## Slide 5: Proposal 2
For LTE-NR coexistence in adjacent spectrum,
  Send an LS to RAN3 to specify the Xn interface and enhanced X2 interface messages that enable coordination between LTE and NR, including
    Signaling related to timing synchronization and SFN
      Note: It is up to RAN3 if this requires new procedures in addition to signaling support
    TDD UL/DL configuration in case of LTE and NR and special subframe configuration in case of LTE