## Slide 1: WF on initial access with SUL
Huawei, HiSilicon, MediaTek, Deutsche Telekom, CATR, CMCC
3GPP TSG RAN WG1 meeting #90 R1- 1714950
Prague, Czech Republic, 21 – 25 August, 2017
Agenda item: 6.1.6

## Slide 2: Background
Agreements:
Specify mechanisms for supporting supplementary Uplink frequency
  Note: SUL herein refers to the case when there is only UL resource for a carrier from NR perspective
  Use SUL as complimentary access link (including from random access point of view) to NR TDD and to NR FDD, where the UE may select PRACH resources either in the NR TDD/FDD uplink frequency or the SUL frequency.
  Note: The SUL frequency can be a frequency shared with LTE UL(at least for the case when NR spectrum is below 6 Ghz).
    Minimize impact to NR physical layer design to enable this co-existence
  Note: whether or not UE has to support simultaneous transmission on uplink frequencies is a separate discussion

## Slide 3: Proposal
For NR UE initial access based on RACH configuration for SUL carrier
  RACH configuration for each SUL carrier is broadcasted in RMSI
  The configuration information for one SUL carrier is sufficient for UEs to complete RACH procedure via only that SUL carrier
  The configuration information for one SUL carrier includes a RSRP threshold. The UE selects that SUL carrier for initial access if the RSRP measured by the UE on the DL carrier where the UE receives RMSI is lower than the RSRP threshold
  If the UE starts its RACH procedure on a SUL carrier, then the RACH procedure is completed with all uplink transmission taking place on that carrier
Sent an LS accommodating above agreement to RAN2