## Slide 1: On the Size of Transmit Buffer
Huawei, HiSilicon
R1-1807736
RAN1#93
Busan, Korea, 21st – 25th May, 2018
Agenda Item: 7.1.3.3.1

## Slide 2: Bit Selection in Current Specs.

## Slide 3: Background - Agreements
Following agreements were made during RAN1 #91 meeting and following up email discussion
Agreements:
For DL, limited buffer rate matching (LBRM) is supported and is applied per HARQ process.
  NR limits transmit buffer corresponding to a largest TBS coded at rate RLBRM.
  RLBRM =½ is supported.
Largest TBS for LBRM for DL should at least take into account UE capability
  Details FFS (e.g., based on UE signalling, gNB configuration w.r.t. highest mod order, etc.)
    Note: this does not prevent the possibility of defining a single largest TBS used for LBRM in Rel-15
Agreements:
For DL LBRM, RLBRM is changed from 1/2 to 2/3.
For uplink,
  Full buffer rate-matching is supported
  Limited buffer rate-matching is also supported via RRC configuration and, when configured, is applied to all HARQ processes
    § NR limits UL transmit buffer corresponding to a largest UL TBS coded at rate RLBRM,UL
    § RLBRM, UL = 2/3.

## Slide 4: Background

## Slide 5: Issue
Assume 2 BWPs are configured, the bandwidth for both BWP is 100MHz. The SCS for BWP1 is 30kHz and the SCS for BWP2 is 60kHz.
Based on current specification, TBSLBRM,30=TBSLBRM,60 is calculated assuming 14 OFDM symbols and 273 PRB, even for 60kHz the maximum PRB is 136.
  Transmit buffer is TBSLBRM,30/ RLBRM=1.5* TBSLBRM,30.
The largest TBS for 30kHz and 60kHz is TBSLargest,30 and TBSLaregest,60 respectably, and TBSLargest,30 ≈ TBSLaregest,60 * 2.
When UE is scheduled at BWP1, the amount data UE needs to buffer and decoding is RLBRM=1.5* TBSLBRM,30 per 0.5ms.
When UE is scheduled at BWP2, the amount data UE needs to buffer and decoding is RLBRM=1.5* TBSLBRM,30 per 0.25ms.
The required throughput at UE side is changed with TTI length!

## Slide 6
This is what we want!

## Slide 7
This is what we get!
UE throughput needs to be double than with longer TTI.
The buffer size is double than expected.

## Slide 8: Why this issue happens
The reason of the problem is not because of SCS change, it is because TBSLBRM is calculated using the larger TTI while UE is scheduled using the shorter TTI.
  For 30kHz, if UE is continuously scheduled with the maximum capability, the throughput of 7-OS scheduling is double than the throughput of 14-OS scheduling.

## Slide 9: Proposal
To solve the issue, one of following alternative can be used
  Alt 1.
    Define the transmit buffer based on UE throughput, e.g., the largest TTI during the scheduled TTI length.
      Corresponding update is provided in Annex.
  Alt 2.
    Make the scheduling limitation so that UE will not be overload.
      If more than one numerology is configured for a cell j, UE is not expected to receive at larger numerology with more than half the maximum data rate of cell j.
      UE is not to expected to receive at a data rate higher than Pmax,j*L/14 if UE is scheduled to receive data on a PDSCH with length L.

## Slide 10: Annex: Text Proposal in R1-1805889