## Slide 1: Discussion on Subframe-based Resource Selection Parameters in Mode-4 NR-V2X
3GPP TSG-RAN WG1 Meeting#94
Gothenburg, Sweden, 20th - 24th August 2018
R1- 1808296

## Slide 2: Introduction
In RAN #80 meeting, the new SID NR-V2X has been agreed with the objective 1 [1], as follows
1: Sidelink design [RAN1, RAN2]:
Identify technical solutions for a NR sidelink design to meet the requirements of advanced V2X services, including
  Study the support of sidelink unicast, sidelink groupcast and sidelink broadcast
  Study NR sidelink physical layer structures and procedure(s)
  Study sidelink synchronization mechanism
  Study sidelink resource allocation mechanism (also including objective 3)
  Study sidelink L2/L3 protocols
Use case groups in NR-V2X
  Vehicle platooning, advanced driving, extended sensors, and remote driving
  Stringent requirements: the maximum end-to-end latency of 3-10ms, the reliability of 99.99-99.999%, the packet size up to 60000 bytes
Introduce subframe based resource selection parameters in mode-4 in addition to channel busy ratio (CBR), for short latency & large size packet

## Slide 3: Case-1: UE Delivers Small Size Packet
For simplicity, selection window contains 16 subframes, each with 4 subchannels. Each packet is mapped on either one or two subchannels
Channel busy ratio (CBR) in sensing window ≈ 0.625
It is not able to deliver a large size packet

## Slide 4: Case-2: UE Delivers Large Size Packet
In the same selection window, each packet is mapped on eight subchannels
Channel busy ratio (CBR) in sensing window ≈ 0.625
It enables to deliver a sporadic or large size packet, but with large latency

## Slide 5: Case-3: UE Delivers Large Size Packet
In the same selection window, each packet is mapped on eight subchannels
Channel busy ratio (CBR) in sensing window ≈ 0.625
It enables to deliver a sporadic or large size packet, with small delay

## Slide 6: Observations
The efficient resource selection cross multi-subframes should be enhanced, in order to deal with sidelink packet transmission with large size.
CBR does not work properly in large size packet delivery, and a new parameter should be further defined.
In order to deliver sporadic packet with stringent latency, each vehicle UE should autonomously select and balance contiguous subchannels in both frequency and time domains, prior to its transmission.

## Slide 7: New Parameter Design
Introduce a new parameter, channel idle ratio (CIR),
Define a maximum contiguous subchannel number ratio in subframe (MCSNRS)
where is the maximum contiguous subchannel number in the
n-th subframe, and N is the total number of subchannels in each subframe.
The CIR, , within M subframes in selection window
where is the threshold of MCSNRS in each subframe, and
The CIR values for case-1, case-2, and case-3, if
  (case-1), (case-2), and (case-3).

## Slide 8: Observation and Proposal
Observation: CIR shows much higher flexibility, whereby each vehicle UE autonomously selects the contiguous subchannels prior to the packet delivery, based on the criterion of maximizing the CIR
Proposal: Study new parameters to deal with the transmissions of the periodic packet with large size and the sporadic packet with stringent latency in NR-V2X
  Introduce the two new parameters, CIR and MCSNRS
  Introduce the threshold of MCSNRS to autonomously control the available contiguous subchannels in transmission resource pool
MCSNRS: maximum contiguous subchannel number ratio in subframe
CIR: channel idle ratio