## Slide 1: WF on Type II overhead reduction
Ericsson, Samsung, Huawei, HiSilicon, Nokia, NSB, Fraunhofer IIS, LGE, Motorola Mobility, lenovo, MediaTek, …
R1-1813883
3GPP TSG-RAN WG1 Meeting #95, Spokane, USA
November 12th – 16th, 2018

## Slide 2: Proposal for Type II framework [1/2]
Precoders for a layer is given by size-matrix
  #SD dimensions
  #FD dimensions
    FFS value and unit of N3
  Precoder normalization: columns of are normalized to norm 1/sqrt(rank)
Spatial domain (SD) compression
  spatial domain basis vectors (mapped to the two polarizations, so in total) selected
  Compression in spatial domain using , where are orthogonal DFT vectors (same as Rel. 15 Type II)
Frequency-domain (FD) compression
  Compression via where , where are size- orthogonal DFT vectors for SD-component
    Number of FD-components or is configurable, FFS value range
  FFS: choose one of the following alternatives
    Alt1. common basis vectors: , i.e. and are identical (i.e., =, )
    Alt2. independent basis vectors: , where , i.e. frequency-domain components (per SD-component) are selected
    Note: or are all selected from the index set from the same orthogonal basis group
  FFS: If oversampled DFT basis or DCT basis is used instead of orthogonal DFT basis
  FFS: Same or different FD-basis selection across layers

## Slide 3: Proposal for Type II framework [2/2]
Linear combination coefficients (for a layer)
  is composed of linear combination coefficients
  FFS if only a subset of coefficients are reported (coefficients not reported are zero).
  FFS if layer compression is applied so that transformed coefficients are used to construct for layer (where the transformed coefficients are the reported quantity)
  FFS quantization/encoding/reporting structure
Note: The terminology “SD-compression” and “FD-compression” are for discussion purposes only and are not intended to be captured in the specification