3GPP TSG-RAN WG2 Meeting #111	R2-20XXXXX

# Electronic, 17 – 28 August 2020

Agenda item:	5.2.1

Source:	ZTE Corporation, Sanechips

Title:	Offline-001 [NR15] NR Stage-2 corrections

Document for:	Discussion & Decision

# Introduction

This is a summary of the following offline discussion on NR R15 stage-2 corrections:

[AT111-e][001][NR15] NR Stage-2 corrections (ZTE)

Scope: Treat R2-2006870, R2-2007222, R2-2007223 (proponents to drive)

Part 1: Decision whether to make corrections, identify agreeable parts.

Deadline: Aug 20, 0900 UTC.

Part 2: For agreeable parts, if any, continuation to agree CRs.

Deadline: Aug 26, 0900 UTC.

This document covers the following contributions submitted to RAN2#111-e meeting:

R2-2006870	Clarification on NCGI	ZTE corporation, Sanechips, Nokia (Rapporteur)	CR	Rel-16	38.300	16.2.0	0260	-	F	NR_newRAT-Core

R2-2007222	Correction on Timing advance group related clarification	vivo	CR	Rel-15	38.300	15.10.0	0270	-	F	NR_newRAT-Core

R2-2007223	Correction on Timing advance group related clarification	vivo	CR	Rel-16	38.300	16.2.0	0271	-	A	NR_newRAT-Core

Companies are invited to provide their views for each issue.

# Discussion: Part 1

## 2.1 Issue #1. Clarification on NCGI

NR Cell Global Identifier (NCGI): used to identify NR cells globally. The NCGI is constructed from the PLMN identity the cell belongs to and the NR Cell Identity (NCI) of the cell. The PLMN ID included in the NCGI should be the first PLMN ID within the set of PLMN IDs associated to the NR Cell Identity in SIB1, following the order of broadcast.

Based on the above definition of NCGI in chapter 8.2, it is clear that the NCGI is constructed from the first PLMN associated with the NR Cell Identity and the NCI. For a PCI, it is allowed to broadcast more than one NCI for the RAN sharing case and thus a PCI can be associated with more than one NCGI.

A physical cell (identified by an SSB associated with an RMSI) is different from a logical cell (identified by an NCGI) and in network sharing, a physical cell can be associated to multiple logical cells. A statement in sub-clause 5.2.4 seems to be mixing these two concepts by limiting that “when an SSB is associated with an RMSI, the SSB corresponds to an individual cell, which has a unique NCGI (see clause 8.2).”

Thus, it's suggested to simplify the statement in 5.2.4 as follows to avoid referring to an NCGI and possibly contradicting section 8 on network identities [1]:

Within the frequency span of a carrier, multiple SSBs can be transmitted. The PCIs of SSBs transmitted in different frequency locations do not have to be unique, i.e. different SSBs in the frequency domain can have different PCIs. However, when an SSB is associated with an RMSI, the SSB is referred to as a Cell-Defining SSB (CD-SSB). A PCell is always associated to a CD-SSB located on the synchronization raster.

Q1) Do companies agree with the above change in R2-2006870 to simplify the statement in 5.2.4?

| Company | Yes/No | Comments (if any) |
| --- | --- | --- |
| Huawei, HiSilicon | Yes |  |
| Nokia | Yes |  |
| MediaTek | Yes, but | We would like to clarify that whether the intention is just to have R16 CR (Note that this R15 AI). We understand that this is correct and apply to both R15 and R16. |
| LG | Yes |  |
| vivo | Yes |  |
| OPPO | Yes |  |
| Intel | Yes |  |
| NEC | Yes |  |
| Qualcomm Incorporated (Masato) | Yes |  |

## 2.2 Issue #2. Clarification on the Timing advance group

In 36.300, it is stated that “for the pTAG the UE uses the PCell in MCG and the PSCell in SCG as timing reference”. In 38.300, it is stated that “For the primary TAG the UE uses the PCell as timing reference”.

Most of the MR-DC specific detailed description has been moved from 38.300. However, there are still references to “SpCell” in 38.300, such as: “when CA duplication is configured for an SRB, one of the logical channels associated to the SRB is mapped to SpCell.” in clause 16.1.3.

Considering that using “PCell” for the primary TAG as timing reference might be misleading (since PSCell is used for SCG), it is suggested to change “PCell” to “SpCell” in the sentence “For the primary TAG the UE uses the PCell as timing reference” in 38.300.

Q2) Do companies agree with the above change in R2-2007222 (Rel-15 CR) and R2-2007223 (Rel-16 mirror CR)?

| Company | Yes/No | Comments (if any) |
| --- | --- | --- |
| Huawei, HiSilicon | Yes |  |
| Nokia | No | This CR is not required as discussed with rapporteur offline. There are many places only Pcell is mentioned since DC is not covered in 300. Pcell/SpCell are not used very consistently in stage 2. |
| MediaTek | Yes, but | We think that it is correct but not essential. No strong view. |
| LG | Yes, but | It would be better to clean up the terminology in 38.300. (not only this place) |
| vivo | Yes | The original description is confusing and we suggest to have this correction to make it clearer. |
| OPPO | Yes, but | Technically it’s correct, however it’s not necessary since DC is not covered by 38.300 |
| Intel | No strong view | It doesn’t seem like an essential correction for Rel-15 stage 2. |
| NEC | Yes but | not essential.. |
| Qualcomm Incorporated (Masato) | Yes | We agree that holistic approach should be taken. |

# Conclusion: Part 1

Based on the above, RAN2 is request to agree the following proposals:

To be added

# Reference

[1] R2-2006870	Clarification on NCGI	ZTE corporation, Sanechips, Nokia (Rapporteur)	CR	Rel-16	38.300	16.2.0	0260	-	F	NR_newRAT-Core

[2] R2-2007222	Correction on Timing advance group related clarification	vivo	CR	Rel-15	38.300	15.10.0	0270	-	F	NR_newRAT-Core

[3] R2-2007223	Correction on Timing advance group related clarification	vivo	CR	Rel-16	38.300	16.2.0	0271	-	A	NR_newRAT-Core