3GPP TSG-RAN WG2 Meeting #111	R2-20XXXXX

# Electronic, 17 – 28 August 2020

Agenda item:	5.4.1.2

Source:	ZTE Corporation, Sanechips

Title:	Offline-006[NR15] Measurements and System Information

Document for:	Discussion & Decision

# Introduction

This is a summary of the following offline discussion on NR R15 stage-2 corrections:

[AT111-e][006][NR15] Measurements and System Information (ZTE)

Scope: Treat R2-2006676, R2-2006677, R2-2008042, R2-2007405-7410, R2-2006878, R2-2007942-7944 (proponents to drive)

Part 1: Decision whether to make corrections, identify agreeable parts. Identify Controversial issues for on-line treatment (if any).

Deadline: Aug 20, 0900 UTC.

Part 2: For agreeable parts, continuation to agree CRs, and possibly LS out.

Deadline: Aug 26, 0900 UTC.

This document covers the following contributions submitted to RAN2#111-e meeting:

Clarification of measCycleSCell

R2-2006676	Clarification of measCycleSCell in measObjectNR	NTT DOCOMO INC.	CR	Rel-15	38.331	15.10.0	1727	-	F	NR_newRAT-Core

R2-2006677	Clarification of measCycleSCell in measObjectNR	NTT DOCOMO INC.	CR	Rel-16	38.331	16.1.0	1728	-	A	NR_newRAT-Core

Channel BW

R2-2008042	SIB1 to include all supported channel bandwidths by the gNB	Qualcomm Incorporated	CR	Rel-16	38.331	16.1.0	1980	-	F	NR_newRAT-Core, TEI16

UAC delay tolerant in shared NW

R2-2007405	Clarification on network specific uac-AccessCategory1-SelectionAssistanceInfo	ZTE corporation, Sanechips, CMCC	discussion	Rel-15	NR_newRAT-Core

R2-2007406	draft CR on network specific uac-AccessCategory1-SelectionAssistanceInfo in TS38.331-R15 solution	ZTE corporation, Sanechips, CMCC	draftCR	Rel-15	38.331	15.10.0	NR_newRAT-Core

R2-2007407	draft CR on network specific uac-AccessCategory1-SelectionAssistanceInfo in TS36.331-R15 solution	ZTE corporation, Sanechips, CMCC	draftCR	Rel-15	36.331	15.10.0	LTE_5GCN_connect-Core

R2-2007408	draft CR on network specific uac-AccessCategory1-SelectionAssistanceInfo in TS38.331-R16 solution	ZTE corporation, Sanechips, CMCC, Nokia	draftCR	Rel-16	38.331	16.1.0	NR_newRAT-Core

R2-2007409	draft CR on network specific uac-AccessCategory1-SelectionAssistanceInfo in TS36.331-R16 solution	ZTE corporation, Sanechips, CMCC, Nokia	draftCR	Rel-16	36.331	16.1.1	LTE_5GCN_connect-Core

R2-2007410	[Draft] LS on UAC Access Category 1 selection	ZTE corporation, Sanechips	LS out	Rel-15	NR_newRAT-Core	To:CT1	Cc:SA2

R2-2006878	Network-specific access barring for delay tolerant service	Lenovo, Motorola Mobility	discussion	Rel-15	NR_newRAT-Core

R2-2007942	ASN.1 issue on uac-AccessCategory1-SelectionAssistanceInfo	vivo	discussion

R2-2007943	38.331 CR for uac-AccessCategory1-SelectionAssistanceInfo	vivo	CR	Rel-16	38.331

R2-2007944	36.331 CR for eab-Param	vivo	CR	Rel-16	36.331	16.1.1	4417	-	F	LTE_5GCN_connect-Core

16.1.0	1947	-	F	NR_newRAT-Core

Companies are invited to provide their views for each issue.

# Discussion: Part 1

## 2.1 Issue #1. Clarification of measCycleSCell [1-2]

When parameter measCycleSCell was introduced in NR spec, the scenario is explicily considered for NR standalone CA case (R2-1813276). While in current field description of measCycleSCell, it states gNB configures the parameter whenever a SCell is configured on the frequency indicated by the measObjectNR, but the field may also be signaled when a SCell is not configured, the wording is ambigous and not clear what is the condition for measCycleSCell configuration. Also, there is still no discussion yet whether this rule is also applicable when only PSCell is configured in the NR part for EN-DC.

Q1) Do companies agree with the proposed clarification that “gNB configures measCycleSCell whenever a SCell is configured on the frequency indicated by the measObjectNR. For EN-DC, gNB need not configure this parameter if only PSCell is configured”?

| Company | Yes/No | Comments (if any) |
| --- | --- | --- |

## 2.2 Issue #2. Clarification on channel BW [3]

In the current spec, for the UE to camp on a cell, it has to run a check on 2 items in the SIB1 for an applicable SCS (for UL and DL):

- UE channel bandwidth is smaller than or equal to the Carrier bandwidth

- UE channel bandwidth is greater than or equal to the initial BWP

If these 2 conditions are satisfied, UE will camp on the cell.

In some cases, these 2 conditions are not be enough, as the cell might not support the channel bandwidth supported by the UE.

As an example:

If UE ONLY supports 30MHz FDD Channel Bandwidth and gNB does not support 30MHz Channel Bandwidth but the gNB advertises carrierBandwidth=50MHz and initial BWP BW = 20MHz, then UE will camp on the NR cell (as the conditions above is met). However, once the UE accesses the NR cell, the network will NOT be able to configure the UE to a valid channel Bandwidth.

This behavior is highly undesirable as it will yield to a connection failure. With current spec, this issue can ONLY be eliminated if the gNB is guaranteed to support all channel Bandwidths (and has done inter-operability tests with UEs) between the initial BWP BW and carrierBandwidth.

Q2.1) Do companies agree that in the current spec there is a lack in the information broadcasted by the SIB1 with respective to the supported channel bandwidth (by network) which might yield to an undesirable behaviour?

| Company | Yes/No | Comments (if any) |
| --- | --- | --- |
| Qcom | Yes | Proponent |

As an approach to resolve this issue, we proposed to enhance the current SIB1, to allow the network to include all supported channel bandwidths. The extension that’s added to SIB1 and the procedural proposed changes, ensure backward compatibility for legacy UE, as this changes will be ignored by legacy UE, and legacy behavior will be applied.

Q2.2) Do companies agree with the solution proposed by the CR?

| Company | Yes/No | Comments (if any) |
| --- | --- | --- |
| Qcom | Yes | Proponent |

Q2.3) if you agreed that there is an issue, but you don’t agree with the proposal, can you please provide an alternate solution?

| Company | Yes/No | Comments (if any) |
| --- | --- | --- |

## 2.3 Issue #3. UAC delay tolerant in shared NW [4-13]

The limitations of the current ASN.1 structure for configuring network specific uac-AccessCategory1-SelectionAssistanceInfo has been discussed at RAN2#110e meeting without reaching agreements.

[AT110-e][076][TEI16] R16 corrections to R15 (ZTE)

Concluding remarks

- 	[076] Chair: There seems to be a common understanding there is indeed a problem with the R15 TS on Allowing different classes of UEs to make choice Delay Tolerant Service (options a b c in SA1 TS) in Network Sharing scenarios. The issue may apply also to eLTE (same ASN.1).

-	[076] Chair: There are requests for further time to check whether to also correct R15, and which solution that is easiest to introduce.

Since there has been common understanding that there is indeed a problem with the R15 TS that if one PLMN wants to configure access barring for delay tolerant services, some other PLMNs sharing the same cell have to configure a “a”, “b” or “c” either via plmnCommon or individualPLMNList even though they do not want to do so because we did not make each entry in the individualPLMNList OPTIONAL.

The potential solutions raised during RAN2#110e and RAN2#111e have been summarized below, trying to find an easier solution (can either be a R15 or R16 solution) for this issue.

- R15 solution: The AS layer forward uac-AccessCategory1-SelectionAssistanceInfo along with the uac-barringInfoSetIndex associated with Access Category 1, if present, to upper layers. The upper layer will select Access Category 1 for concerned UE when both uac-AccessCategory1-SelectionAssistanceInfo along with the uac-barringInfoSetIndex associated with Access Category 1 are provided.

As specified in the following table in TS24.501, the NAS layer will select Access Category 1 for the concerned UE when uac-AccessCategory1-SelectionAssistanceInfo is configured. Based on the existing ASN.1, as mentioned in 2.1, some PLMN are forced to configure this field even they do not want to.

Table 4.5.2.2: Mapping table for access categories

| Rule # | Type of access attempt | Requirements to be met | Access Category |
| --- | --- | --- | --- |
| 4 | Access attempt for delay tolerant service | (a) UE is configured for NAS signalling low priority or UE supporting S1 mode is configured for EAB (see the "ExtendedAccessBarring" leaf of NAS configuration MO in 3GPP TS 24.368 [17] or 3GPP TS 31.102 [22]) where "EAB override" does not apply, and (b): the UE received one of the categories a, b or c as part of the parameters for unified access control in the broadcast system information, and the UE is a member of the broadcasted category in the selected PLMN or RPLMN/equivalent PLMN (NOTE 3, NOTE 5, NOTE 6, NOTE 7, NOTE 8) | 1 (= delay tolerant) |

One candidate R15 solution without changing the ASN.1 is to change the behaviour in NAS layer and specify that Access Category 1 for concerned UE when both uac-AccessCategory1-SelectionAssistanceInfo along with the uac-barringInfoSetIndex associated with Access Category 1 are provided. In this way, a PLMN not willing to configure Access Category will not configure uac-barringInfoSetIndex for Access Category 1 and the upper layer will never select Access Category 1.

Although this solution will not change the ASN.1, it will still change the UE behaviour in both AS layer (e.g. UE has to forward the uac-barringInfoSetIndex for Access Category 1 to upper layer) and NAS layer (e.g. UE should also take the uac-barringInfoSetIndex for Access Category 1 into consideration when selecting Access Category 1).

In addition, based on the existing unified access control procedure, if the uac-barringInfoSetIndex for a certain Access Category is not configured, UE will consider the access attempt is allowed. If we following the above R15 solution, the following configuration cannot be achieved: A PLMN would like to configure Access Category 1 and would like to allow all the access attempts for AC1 (i.e. 100% allowed), as the maximum probability that access attempt would be allowed can be configured via uac-barringInfoSetIndex is 95%.

Considering that some network vendors may have not configure Access Category 1(e.g. the uac-AccessCategory1-SelectionAssistanceInfo is not configured for any PLMN) in R15 yet, R16 solution can also be considered to avoid changing the R15 UE behaviour.

- R16 solution: Introduce new fields to indicate UAC-AccessCategory1-SelectionAssistanceInfo is not applied or not configured for a certain PLMN.

- Option 1: Introduce UAC-AccessCategory1-SelectionAssistanceInfo-v16xy with value {a, b, c, notConfigured} to replace the UAC-AccessCategory1-SelectionAssistanceInfo.

If a PLMN does not want to configure access barring for delay tolerant service, the corresponding UAC-AccessCategory1-SelectionAssistanceInfo-v16xy will be set to “notConfigured”.

- Option 2: Introduce UAC-AccessCategory1-SelectionAssistanceInfoExt-v16xy with value “notConfigured” as an additional candidate value for Access Category1 selection assistance information.

If the newly introduced UAC-AccessCategory1-SelectionAssistanceInfoExt-v16xy field is present, the UE should ignore the legacy value provided by UAC-AccessCategory1-SelectionAssistanceInfo and consider the access barring for delay tolerant service is not configured.

- Option 3: Introduce individualPLMNList-v16xy containing a list of network index and the associated UAC-AccessCategory1-SelectionAssistanceInfo. The network index is included only when the correspoding UAC-AccessCategory1-SelectionAssistanceInfo with value a/b/c needs to be configured.

- Option 4: Introduce uac-AccessCategory1-SelectionAssistanceInfo-PresenceBitmap-r16 to indicate whether the value (e.g. a, b or c) configured via plmnCommon or individualPLMN for each PLMN is valid or not.

Q3.1) To allow the flexibility for a certain PLMN not to configure the uac-AccessCategory1-SelectionAssistanceInfo field for RAN sharing case, which solution do companies prefer, R15 solution or R16 solution?

- R15 solution: The AS layer forward uac-AccessCategory1-SelectionAssistanceInfo along with the uac-barringInfoSetIndex associated with Access Category 1, if present, to upper layers. The upper layer will select Access Category 1 for concerned UE when both uac-AccessCategory1-SelectionAssistanceInfo along with the uac-barringInfoSetIndex associated with Access Category 1 are provided.

- R16 solution: Introduce new fields to indicate UAC-AccessCategory1-SelectionAssistanceInfo is not applied or not configured for a certain PLMN.

| Company | R15/R16 solution | Comments (if any) |
| --- | --- | --- |

Considering that the R15 solution will change the category selection behavior in NAS layer, an LS should be sent to CT1 to request changes in TS24.501 if R15 solution is selected.

Q3.2) If R15 solution is preferred in Q3.1, do companies agree that an LS should be sent to CT1 to request changes in their specs?

| Company | Yes/No | Comments (if any) |
| --- | --- | --- |

Q3.3) If R16 solution is preferred in Q3.1, which detailed option do companies prefer?

- Option 1: Introduce UAC-AccessCategory1-SelectionAssistanceInfo-v16xy with value {a, b, c, notConfigured} to replace the UAC-AccessCategory1-SelectionAssistanceInfo.

- Option 2: Introduce UAC-AccessCategory1-SelectionAssistanceInfoExt-v16xy with value “notConfigured” as an additional candidate value for Access Category1 selection assistance information.

- Option 3: Introduce individualPLMNList-v16xy containing a list of network index and the associated UAC-AccessCategory1-SelectionAssistanceInfo. The network index is included only when the corresponding UAC-AccessCategory1-SelectionAssistanceInfo with value a/b/c needs to be configured.

- Option 4: Introduce uac-AccessCategory1-SelectionAssistanceInfo-PresenceBitmap-r16 to indicate whether the value (e.g. a, b or c) configured via plmnCommon or individualPLMN for each PLMN is valid or not.

| Company | Option 1/2/3/4 | Comments (if any) |
| --- | --- | --- |

The same problem exists in uac-AC1-SelectAssistInfo configuration in SIB25 for EUTRA connected to 5GC in 36.331 as the same structure is applied. The same solution (R15 solution or R16 solution), concluded for NR after down selection, should also be applied in Access Category 1 handling for EUTRA connected to 5GC.

Q3.4) Do companies agree that the same solution should be applied for Access Category 1 handling for NR and EUTRA connected to 5GC?

| Company | Yes/No | Comments (if any) |
| --- | --- | --- |

# Conclusion: Part 1

Based on the above, RAN2 is request to agree the following proposals:

To be added

# Reference

[1] R2-2006676	Clarification of measCycleSCell in measObjectNR	NTT DOCOMO INC

[2] R2-2006677	Clarification of measCycleSCell in measObjectNR	NTT DOCOMO INC

[3] R2-2008042	SIB1 to include all supported channel bandwidths by the gNB	Qualcomm

[4] R2-2007405	Clarification on network specific uac-AccessCategory1-SelectionAssistanceInfo	ZTE corporation, Sanechips, CMCC

[5] R2-2007406	draft CR on network specific uac-AccessCategory1-SelectionAssistanceInfo in TS38.331-R15 solution	ZTE corporation, Sanechips, CMCC

[6] R2-2007407	draft CR on network specific uac-AccessCategory1-SelectionAssistanceInfo in TS36.331-R15 solution	ZTE corporation, Sanechips, CMCC

[7] R2-2007408	draft CR on network specific uac-AccessCategory1-SelectionAssistanceInfo in TS38.331-R16 solution	ZTE corporation, Sanechips, CMCC, Nokia

[8] R2-2007409	draft CR on network specific uac-AccessCategory1-SelectionAssistanceInfo in TS36.331-R16 solution	ZTE corporation, Sanechips, CMCC, Nokia

[9] R2-2007410	[Draft] LS on UAC Access Category 1 selection	ZTE corporation, Sanechips

[10] R2-2006878	Network-specific access barring for delay tolerant service	Lenovo, Motorola Mobility

[11] R2-2007942	ASN.1 issue on uac-AccessCategory1-SelectionAssistanceInfo	vivo

[12] R2-2007943	38.331 CR for uac-AccessCategory1-SelectionAssistanceInfo	vivo

[13] R2-2007944	36.331 CR for eab-Param	vivo