3GPP TSG-RAN2 Meeting #111 Electronic 	Draft of R2- 2008131

# 17th August – 28th August 2020

Agenda Item:	4.5

Source: 	Samsung

Title:  	Summary of offline 201 - LTE Miscellaneous Rel-15/16 corrections

Document for:	Discussion and decision

# Introduction

[AT111-e#201][LTE] LTE Miscellaneous Rel-15/16 corrections (Samsung)

Scope:

    - Discuss the CRs under AI 4.5, 7.1.3 and 7.5 marked for this email discussion

Intended outcome:

    - Discussion summary in R2-2008131 (by email rapporteur)

    - Agreeable CRs by proponents (if revised versions are required, proponents should obtain Tdoc numbers from session chair or RAN2 secretary to provide those)

Deadline for providing comments and for rapporteur inputs:

    - Initial deadline (for companies' feedback):  Wednesday 2020-08-19 10:00 UTC

    - Initial deadline (for rapporteur's summary in R2-2008131):  Thursday 2020-08-20 08:00 UTC

    - Deadline for CR finalization: Wednesday 2020-08-26 07:00 UTC

# PDU generation for UL spatial multiplexing (Rel-14)

In RAN2#110 meeting, RAN2 made some concensus on that the intent of option 2 of R2-2005551 (i.e. UE generates two MAC PDUs as long as one of the two MAC PDUs comprises available data when receiving two UL grants for UL spatial multiplexing) is agreeable. Below CRs provide the possible options to solve this issue.

R2-2007719	Correction on PDU generation for UL spatial multiplexing – Option 1	ASUSTeK	CR	Rel-14	36.321	14.12.0	1497	-	F	LTE_LATRED_L2-Core, TEI14

R2-2007720	Correction on PDU generation for UL spatial multiplexing – Option 2	ASUSTeK	CR	Rel-14	36.321	14.12.0	1498	-	F	LTE_LATRED_L2-Core, TEI14

R2-2007721	Correction on PDU generation for UL spatial multiplexing – Option 1	ASUSTeK	CR	Rel-15	36.321	15.9.0	1499	-	A	LTE_LATRED_L2-Core, TEI14

R2-2007722	Correction on PDU generation for UL spatial multiplexing – Option 2	ASUSTeK	CR	Rel-15	36.321	15.9.0	1500	-	A	LTE_LATRED_L2-Core, TEI14

R2-2007723	Correction on PDU generation for UL spatial multiplexing – Option 1	ASUSTeK	CR	Rel-16	36.321	16.1.0	1501	-	A	LTE_LATRED_L2-Core, TEI14

R2-2007724	Correction on PDU generation for UL spatial multiplexing – Option 2	ASUSTeK	CR	Rel-16	36.321	16.1.0	1502	-	A	LTE_LATRED_L2-Core, TEI14

Q1: Do you agree some clarifications are needed in the specification to solve the problems (i.e. If there is insufficient available data, MAC may generate only one MAC PDU for a given TTI although receiving two UL grants for UL spatial multiplexing.)?

- Yes

- No (i.e. NW implementation can solve this problem)

| Company | Answer | Detailed Comments |
| --- | --- | --- |
| ASUSTeK | Yes | We reach the following conclusion in RAN2#110-e: Intent of option 2 is agreeable, but no consensus on what to capture Intent of option 2 is to specify a UE solution, i.e. we won’t rely on NW implementation to solve the issue. The only thing left for discussion is what to capture in the standard (the following Q2). |
| LG | No | Referring to NOTE in S5.4.3, the UE can process multiple UL grants at one TTI as one resource by summing the multiple UL grants. Accordingly, the UE by itself can put available data into two separate UL grants. |
| Samsung | Yes | We share the problem. We prefer to clarify the UE behavior. |
| Nokia | Yes |  |
| Ericsson | No | We think, regarding the fact that the discussion was postponed, that there was no conclusion e.g. on whether a CR is needed. Note that the conclusion from the email discussion report captured in R2-2005731 in the last meeting was “Some companies think the intent is correct but others consider this can be left up to UE and/or network implementation, as NOTE will not specify anything. |
| HW | Neutral | We tend to agree with the intention but we also think either rely on NW implementation (do not configure UP skipping in case of UL spatial) or UE implementation (generate two packets) can solve this issue. However if the majority supports to clearly clarify this issue, we are fine to support to add a note in MAC as proposed by option 1. |

Q2: If your answer for Q1 is Yes, which option is preffered? And if you have further comments on the suggested descriptions in the CRs, please provide the reqeusted changes.

- Option 1: Add a NOTE

- Option 2: Update the normative text

| Company | Answer | Detailed Comments |
| --- | --- | --- |
| ASUSTeK | Option 1 or Option 2 | We would like to conclude the issue by adopting either option 1 or option 2. |
| Samsung | Option 1 | Adding Note seems enough. |
| Nokia | Option 2 | But The proposed wording is a bit problematic since “If at least one MAC PDU is to be generated for the HARQ entity for this TTI” is not specific to UL spatial multiplexing case, it also with carrier aggregation. The UE should not be required to generate all the TBs for the same TTI for CA case. |
| ASUSTeK |  | About the proposed wording, whether “at least one MAC PDU” or “all the MAC PDU(s)” is for the same HARQ entity and, according to the spec, is for the same Serving Cell. |

# Miscellaneous small corrections (Rel-15)

R2-2007579	Corrections on idle mode measurements   Ericsson        CR      Rel-15		36.300

R2-2007589	Corrections on idle mode measurements   Ericsson Inc.   	CR      Rel-15		36.331

| Company | Agree as is; Agree with changes; Disagree | Detailed Comments |
| --- | --- | --- |
| Samsung | Agree for R2-2007579; Disagree for R2-2007589 | For R2-2007589, proposed NOTE seems not needed and it makes more confusion for UE implementation. Other changes are minor so they can be merged into the Rapporteur CR. |
| Nokia | Agree | Changes seems to be correct although not critical but as said nothing wrong with the change so if people see this necessary we are fine |
| Lenovo | Agree with changes | 1, To 36.300 Rel-15 CR 7579: “inactive state” should be added as measurement configuration provided by field measIdleConfigSIB-r15 applies to RRC_INACTIVE as well. Furthermore, for the missing Rel-16 CR the description needs to be further extended by adding idle/inactive measurements for NR (due to field measIdleConfigSIB-NR-r16). 2. To 36.331 CR 7589: On the new note in 5.6.20.2: We think that it is not needed as there is already a note saying “How the UE performs measurements in IDLE mode is up to UE implementation as long as the requirements in TS 36.133 [16] are met for measurement reporting.” On the change of description of SIB5: “inactive state” should be added as measurement configuration provided by field measIdleConfigSIB-r15 applies to RRC_INACTIVE as well. Furthermore, for the missing Rel-16 CR the description needs to be further extended by adding idle/inactive measurements for NR (due to field measIdleConfigSIB-NR-r16). There is no need for the changes in IE MeasResults due to the fact that field measResultListIdle is not defined in IE MeasResults but in RRCConnectionResumeComplete and UEInformationResponse. That means, the measured results are reported in those messages and not via IE MeasResults. |
| HW | Disagree | For R2-2007589, we share the same view as Samsung. For R2-2007579, we don’t think this stage 2 clarification is needed as we will clarify in 331 spec that SIB5 includes information for configuration of idle mode measurements. |

# Editorial MAC changes

R2-2007655	Editorial changes	Ericsson	CR	Rel-16	36.321

| Company | Agree as is; Agree with changes; Disagree | Detailed Comments |
| --- | --- | --- |
| Samsung | Agree |  |
| Nokia | Agree |  |
| ASUSTeK | Agree |  |
| HW | Agree |  |

# Editorial RRC changes

R2-2007843	Minor changes collected by Rapporteur	Samsung	CR	Rel-15	36.331

| Company | Agree as is; Agree with changes; Disagree | Detailed Comments |
| --- | --- | --- |
| Samsung | Agree | If there will be some more editorials from other CRs, this CR can be updated. |
| Nokia | Agree |  |
| ASUSTeK | Agree |  |
| Lenovo | Agree with changes | Cover page issues: “Consequences if not approved” is empty; in “Other specs affected” the boxes “N” need to be ticked. Further minor Rel-15 issues can be fixed: In subclause 2: in reference [88] add “for control” in the title of the RAN1 spec: [88] 3GPP TS 38.213: "NR; Physical layer procedures for control". 6.3.6: IE FlightPathInfoReportConfig: due to typos in the word “speficies” it should be corrected to “specifies”. “The IE FlightPathInfoReportConfig speficies flight path information report configuration.” 6.3.6: For IE GNSS-ID the header “GNSS-ID information element” is missing. 6.3.6: For IE SBAS-ID the header “SBAS-ID information element” is missing. |
| HW | Agree |  |

R2-2007844	Minor changes collected by Rapporteur	Samsung	CR	Rel-16	36.331

| Company | Agree as is; Agree with changes; Disagree | Detailed Comments |
| --- | --- | --- |
| Samsung | Agree | If there will be some more editorials from other CRs, this CR can be updated. |
| Nokia | Agree |  |
| ASUSTeK | Agree |  |
| Lenovo | Agree with changes | Same cover page issues as in 7843. Further Rel-15 issues as addressed for 7843 can be added. Further minor Rel-16 issue can be fixed: 6.2.2: RRCConnectionResumeComplete-v1610-IEs the suffix of measResultListIdle-r15 needs to be corrected to “-r16”. In A.3.8 for field2-rX the suffix "-rX" can be removed. |
| HW | Agree |  |

# Conclusions

TBD