3GPP TSG RAN WG2 Meeting #115-e	                                        R2-2108931

# Electronic, 16th – 27th August 2021

Agenda item:		4.4

Source:			Lenovo

Title:		Report from email discussion [AT115-e][601][POS] AI 4.4 Positioning corrections Rel-15 and earlier (Lenovo)

Document for:	 	Discussion and decision

# Introduction

This report summarizes the email discussion below that took place during RAN2#115-e meeting:

- [AT115-e][601][POS] AI 4.4 Positioning corrections Rel-15 and earlier (Lenovo)

Scope: Handle the CRs in the following tdocs and determine conclusions:

- R2-2107261/R2-2107262

- R2-2107784

- R2-2107785/R2-2107786

Note: R2-2107785 and R2-2107786 were submitted under AI 5.5 and relate to TS 37.355, but are functionally shadows of R2-2107784

Intended outcome: Agreed CRs (without comeback), report in R2-2108931

Deadline:  Tuesday 2021-08-24 0800 UTC

# Reference

The following documents are treated in this email discussion:

[1]	R2-2107260	Further discussion on Positioning SI message scheduling for eMTC	Lenovo, Motorola Mobility		discussion	Rel-15	LCS_LTE_acc_enh-Core

[2]	R2-2107261	Addition of scheduling restrictions of positioning SI messages for eMTC	Lenovo, Motorola Mobility	CR	Rel-15	36.331	15.14.0	4691	-	F	LCS_LTE_acc_enh-Core

[3]	R2-2107262	Addition of scheduling restrictions of positioning SI messages for eMTC	Lenovo, Motorola Mobility	CR	Rel-16	36.331	16.5.0	4692	-	A	LCS_LTE_acc_enh-Core

[4]	R2-2107784	Correction on ProvideCapabilities and ProvideLocationInformation	Samsung	CR	Rel-14	36.355	14.7.0	0258	-	F	TEI14

[5]	R2-2107785	Correction on ProvideCapabilities and ProvideLocationInformation	Samsung	CR	Rel-15	37.355	15.2.0	0316	-	A	TEI14

[6]	R2-2107786	Correction on ProvideCapabilities and ProvideLocationInformation	Samsung	CR	Rel-16	37.355	16.5.0	0317	-	A	TEI14

# Contact information

| Company | Contact Name, Email |
| --- | --- |
| Nokia | mani.thyagarajan@nokia.com |
| Huawei, HiSilicon | yinghaoguo@huawei.com |
| CATT | lijianxiang@datangmobile.cn |
| Ericsson | Ritesh.shreevastav@ericsson.com |
| Lenovo | hchoi5@lenovo.com |
| ZTE | pan.yu24@zte.com.cn |

# Discussion

## Positioning SI message scheduling for eMTC

First discussion on the issue on missing scheduling restrictions of positioning SI messages for eMTC UEs (BL/CE UEs) took place in last RAN2#114-e meeting but following discussion there was no consensus on the issue. However, proponent thinks that the issue raised is still valid and requires further clarification.

In [1] further arguments are provided on how positioning assistance data are broadcast for eMTC UEs (BL/CE UEs) acc. to the RRC specification. However, referring to the discussion from last meeting it seems that companies have different understanding on the method:

- Understanding 1: If positioning SI messages are broadcast to BL/CE UEs in an LTE cell, then they are transmitted in the BR version of SI messages (SystemInformation-BR-r13) and the scheduling information of the positioning SI messages (posSchedulingInfoList-r15) is sent in the BR version of SIB1 (SystemInformationBlockType1-BR-r13).

- Understanding 2: If positioning SI messages are broadcast to BL/CE UEs in an LTE cell, then they are transmitted in the legacy version of SI messages (SystemInformation) and the scheduling information of the positioning SI messages (posSchedulingInfoList-r15) is sent in the legacy SIB1.

BL/CE UEs are operated with a limited bandwidth of 1.4 MHz (6 PRBs) in an LTE cell and in Figure 1 below an example of eMTC operation in an LTE cell with system bandwidths larger than 1.4 MHz is shown. The eMTC UEs are operated in the set of narrowbands which are configured in the LTE cell.

Figure 1: Example of eMTC operation in an LTE cell

Question 1a: Companies are asked for their understanding on the broadcast of assistance data for eMTC UEs (BL/CE UEs).

| Company | Understanding 1 or 2 | Additional comments |
| --- | --- | --- |
| Nokia |  | As we commented in the last meeting, this issue is best discussed in eMTC session since we in positioning session did not decide whether broadcast assistance data is supported or not for eMTC UEs and whether BR version or legacy version of SI message is to be used for broadcast of positioning assistance data to eMTC UEs. However, to me Understanding 1 seems to make sense. |
| Huawei, HiSilicon | Understanding 1 |  |
| CATT | Understanding 1 |  |
| Ericsson | Understanding 1 |  |
| Qualcomm | Understanding 1 |  |
| Lenovo | Understanding 1 |  |
| ZTE | Understanding 1 |  |
| Intel |  | Same view as Nokia. This issue should be confirmed in eMTC session. |
| vivo | Understanding 1 |  |

The following questions are related to Understanding 1.

If the BR version of SI messages (SystemInformation-BR-r13) and SIB1 (SystemInformationBlockType1-BR-r13) are used, then restrictions to the scheduling of SI messages are sent by schedulingInfoList-BR-r13 within the bandwidthReducedAccessRelatedInfo-r13 IE:

- si-Narrowband-r13: index of a narrowband used to broadcast the SI message towards BL/CE UEs.

- si-TBS-r13: transport block size used to broadcast the SI message towards BL/CE Ues.

But as pointed out in [1], the restrictions given by schedulingInfoList-BR-r13 have been specified only for schedulingInfoList (without suffix). However, proponent thinks that the scheduling restrictions need to apply for posSchedulingInfoList-r15 as well but schedulingInfoList-BR-r13 is currently not applicable for positioning SI messages due to the fact that the number and order of entries in schedulingInfoList-BR-r13 are tied to the number and order of entries in schedulingInfoList. And for Positioning it can be assumed that the number of scheduled positioning SI messages is independent from the ones in schedulingInfoList. In order to solve this issue, two options have been addressed in [1] (but the list of options may not exhaustive):

- Option 1: Introduce a new field posSchedulingInfoList-BR-r15 for adding the missing scheduling restrictions for BL Ues and Ues in CE.

- Option 2: Specify a default narrowband and TBS to be used for broadcasting Positioning SI messages towards BL Ues and Ues in CE.

Question 1b: Do companies agree that scheduling restrictions given by schedulingInfoList-BR-r13 are missing for scheduling of positioning SI messages to BL/CE Ues? If the answer is “yes”, how should this issue be solved?

| Company | Yes/No | Additional comments |
| --- | --- | --- |
| Nokia | Yes | Option 1 sounds good, but this must be discussed in eMTC session. |
| Huawei, HiSIlicon | Yes | Option1 should be adopted |
| CATT | Yes | Option1 seems better. |
| Ericsson | Yes | Option 1 |
| Qualcomm | Yes | Option 1. |
| Lenovo | Yes | Option 1 |
| ZTE | Yes | Option 1 is straightforward |
| Intel | Yes | It should be confirmed in eMTC session. |
| vivo | Yes | Option1 and should be confirmed in eMTC session. |

In the CRs [2], [3] a solution acc. to Option 1 has been provided to introduce the scheduling restrictions for positioning SI messages to BL/CE UEs.

Question 1c: Are the changes in the CRs agreeable or do they need further review, e.g. by eMTC experts?

| Company | Agreeable / Further review needed | Additional comments |
| --- | --- | --- |
| Nokia | Further review needed | Again, the issue and the CRs needs to be discussed in eMTC session. |
| Huawei, HiSilicon | Agreeable |  |
| CATT |  | The CR needs to be modified considering on the extensions, e.g., Extending the SystemInformationBlockType1-v15xy-IEs within the SystemInformationBlockType1-v12j0-IEs is not accurate. [Lenovo] We used the late NCE branch for introducing SystemInformationBlockType1-v15xy-IEs due to the fact that in R16 the regular NCE branch is already taken by SystemInformationBlockType1-v1610-IEs. [CATT2] Ok, we can use late NCE branch. But whether we should add a late NCE container between R12 and R15 for potential late R12, R13 and R14 late NCE? Just like what we had done in SystemInformationBlockType1-v10x0-IEs. SystemInformationBlockType1-v10x0-IEs ::= SEQUENCE { -- This field is only for late non-critical extensions from Rel-10 or Rel-11 onwards lateNonCriticalExtension OCTET STRING OPTIONAL, nonCriticalExtension SystemInformationBlockType1-v12j0-IEs OPTIONAL } |
| Ericsson | Agreeable |  |
| Qualcomm | Agreeable |  |
| Lenovo | Agreeable | But to address the comments from Nokia and CATT it is acceptable to us to let the eMTC experts do the final review. At least we suggest that the CRs are endorsed in the Positioning session. |
| ZTE | Further review needed | Agree with Nokia |
| Nokia | Further review needed | Again with Nokia. |
| vivo | Further review needed | Need to further discuss in eMTC session. |

## Correction on ProvideCapabilities and ProvideLocationInformation

In the CRs [4], [5], [6] it is proposed to replace the word "response" by "message" in the procedure text for transmitting ProvideCapabilities (clause 5.1.4) and ProvideLocationInformation message (clause 5.3.4) as shown below:

5.1.4 Transmission of LPP Provide Capabilities When triggered to transmit a ProvideCapabilities message, the target device shall: 1> for each positioning method whose capabilities are to be indicated: 2> set the corresponding IE to include the device's capabilities; 2> if OTDOA capabilities are to be indicated: 3> include the IE supportedBandListEUTRA; 1> deliver the message to lower layers for transmission.

5.3.4 Transmission of Provide Location Information When triggered to transmit ProvideLocationInformation message, the target device shall: 1> for each positioning method contained in the message: 2> set the corresponding IE to include the available location information; 1> deliver the message to lower layers for transmission.

Proponent thinks that the word “response” is misleading considering the fact that the target device is allowed to provide unsolicited capabilities (see clause 5.1.2) and unsolicited location information (see clause 5.3.2) to the location server.

Question 2a: Do companies agree on the proposed changes to ProvideCapabilities and ProvideLocationInformation?

| Company | Yes/No | Additional comments |
| --- | --- | --- |
| Nokia | No | This is not an essential correction. Agree that the term “response” may imply that it covers only the case when a request is received by the UE but the procedure is written to cover the “unsolicited” case also by use of the text “When triggered to transmit…” where triggered could also refer to UE internal trigger to send ProvideCapabilities/ProvideLocationInformation unsolicited. But this can also be viewed as a response to UE internal trigger to send unsolicited. |
| Huawei, HiSilicon | No | The correction is not critical |
| CATT | No strong view | This is not an essential correction. |
| Qualcomm | No | Same view as Nokia. |
| Lenovo | No | We agree with Nokia. |
| ZTE | No | Not essential problem |
| Intel | No | Not essential. |
| vivo | No | Not essential. |

The procedures in clause 5.1.4 and 5.3.4 are specified since Rel-9 but it is proposed to make the changes from Rel-14.

Question 2b: If the answer to Question 2a is “yes” from which release should the changes be made, i.e. from Rel-14 or later?

| Company | Release (Rel-14, Rel-15, Rel-16) | Additional comments |
| --- | --- | --- |

# Conclusion

Based on company’s feedback the following proposals are made:

<To be updated>