# 3GPP TSG RAN WG2 Meeting #117-e      	                    R2-220xxxx
E-Meeting, February 21 – March 03, 2022

Agenda item: 	8.22.3.2.2

Source:	Apple

Title: 	Summary of [AT117-e][019][MGE] Network Controlled Small Gap (Apple)

WID/SID:	NR_MG_enh-Core – Release 17

Document for:	Discussion and Decision

# Introduction

This is the summary of the following email discussion.

[AT117-e][019][MGE] Network Controlled Small Gap (Apple)

Scope: Based on R2-2203713, determine agreeable parts, points for discussion, open issues if needed. Converge as far as possible to reduce the need for on-line discussion.

Intended outcome: Report

Deadline: In time for on-line CB W2 Tuesday (please feedback before W1 Friday, Feb. 25, End of Day local time)

# Reference

[1] R2-2203713 [Pre117-e][019][MGE] AI summary of 8.22.3.2.2 Network Controlled Small Gap (Apple) Apple

[2] R2-2202323 Discussion on NCSG	vivo	discussion	Rel-17	NR_MG_enh-Core

[3] R2-2202512 RAN2 impact from NCSG	Apple	discussion	Rel-17	NR_MG_enh-Core

[4] R2-2202648 Remaining issues on NCSG	ZTE Corporation, Sanechips	discussion	Rel-17	NR_MG_enh-Core

[5] R2-2202874 Discussion on open issue of NCSG	MediaTek Inc.	discussion

[6] R2-2202891 Discussion on NCSG	Huawei, HiSilicon	discussion	Rel-17	NR_MG_enh-Core

[7] R2-2202945 Discussion on remaining issues of NCSG	CATT	discussion	Rel-17	NR_MG_enh-Core

[8] R2-2203012 On Network Controlled Small Gaps	Samsung	discussion

[9] R2-2203261 Discussion on open issues for NCSG	Nokia, Nokia Shanghai Bell	discussion	Rel-17	NR_MG_enh-Core

[10] R2-2203449 Network Controlled Small Gap	Ericsson	discussion	Rel-17	NR_MG_enh-Core

[11] R2-2203503 SSB index derivation for NCSG	Qualcomm Incorporated	CR	Rel-17	38.331	16.7.0	2964	-	B	NR_MG_enh-Core

# Contact info

| Company Name | Contact Person | Email Address |
| --- | --- | --- |
| MediaTek | Felix Tsai | Chun-fan.tsai@mediatek.com |
| Huawei, HiSilicon | Lili Zheng | zhenglili4@huawei.com |
| ZTE | LiuJing | liu.jing30@zte.com.cn |
| Samsung | Aby K Abraham | Aby.abraham@samsung.com |
| Intel | Candy yiu | Candy.yiu@intel.com |
| Apple | Yuqin Chen | yuqin_chen@apple.com |
| vivo | Xiaodong Yang | Yangxiaodong5g@vivo.com |
| OPPO | Shukun Wang | wangshukun@oppo.com |
| Ericsson | Felipe Arraño Scharager | felipe.arrano.scharager@ericsson.com |
| LGE | SangWon Kim | sangwon7.kim@lge.com |
| CATT | Jie Shi | shijie@catt.cn |
| Nokia | Ping Yuan | Ping.1.yuan@nokia-sbell.com |

# Discussion

## Open issue N1-6: Derivation of SSB indexes of target cell on inter-frequency from serving cell timing

Issue 1: Whether and how to enable it in RRC signaling

In R2-2203713 [1], the following summary and proposal is provided by the moderator.

Summary: 8/10 companies proposed to support the enabling of derivation of SSB indexes of target cell on inter-frequency from serving cell timing. 2/10 companies do not support to enable it. Regarding signaling details, some minor differences between the proposals are observed: One new field referring to ServCellIndex, or two new fields with one to indicate the enabling of feature (Boolean) and one to refer to ServCellIndex. Carried under SSB-ConfigMobility in MeasObjectNR, or under MeasObjectNR Detailed field name Considering that RAN4 explicitly requests RAN2 to design the signaling to enable this feature and the large support, the rapporteur tends to have the following proposal. Proposal 1: Agree to support enabling derivation of SSB indexes of target cell on inter-frequency from serving cell timing. FFS on ASN.1 details.

Question 1: Do companies agree to support enabling derivation of SSB indexes of target cell on inter-frequency from serving cell timing?

| Company | Yes/No | Comments |
| --- | --- | --- |
| MediaTek | Prefer no | It looks like NCSG could function normally without this enhancement. But we are fine to follow majority |
| Huawei, HiSilicon | Yes | It can help minimize scheduling restriction. |
| ZTE | Yes, but | Although we think this new field is not very useful as expected (see our response to Q4), we won’t object as RAN4 already agreed this. |
| Samsung | Yes |  |
| Intel | Yes |  |
| Apple | Yes |  |
| vivo | OK |  |
| OPPO | Yes |  |
| Ericsson | No | Not enabling this still allows for acceptable delays and we don’t see a real motivation to introduce the signaling proposed by RAN4. However, we don’t have a strong view against it either. |
| LGE | Yes | As agreed by RAN4. |
| CATT | Yes | Follow RAN4’s agreement. |
| Nokia | Yes |  |

Question 2: Regarding ASN.1 details, please companies indicate your preference.

- Approach 1: Introducing one new field (e.g, deriveSSB-IndexFromCell-Inter-r17) which refers to ServCellIndex

- Approach 2: Introducing two new fields, with one to indicate the enabling of feature (Boolean) and the other one to refer to ServCellIndex

| Company | Approach 1/2 | Comments |
| --- | --- | --- |
| MediaTek | Approach 1 | Seems unnecessary to have two fields |
| Huawei, HiSilicon | Approach 1 | One new field is enough: SSB-ConfigMobility::= SEQUENCE { ssb-ToMeasure SetupRelease { SSB-ToMeasure } OPTIONAL, -- Need M deriveSSB-IndexFromCell BOOLEAN, ss-RSSI-Measurement SS-RSSI-Measurement OPTIONAL, -- Need M ..., [[ ssb-PositionQCL-Common-r16 SSB-PositionQCL-Relation-r16 OPTIONAL, -- Cond SharedSpectrum ssb-PositionQCL-CellsToAddModList-r16 SSB-PositionQCL-CellsToAddModList-r16 OPTIONAL, -- Need N ssb-PositionQCL-CellsToRemoveList-r16 PCI-List OPTIONAL -- Need N ]], [[ deriveSSB-IndexFromCell-Inter-r17 ServCellIndex OPTIONAL -- Need M ]] } |
| ZTE | Approach 1 |  |
| Samsung | Approach 1 | Presence of new field can very well indicate the enabling of feature. So flag is redundant. |
| Intel | Approach 1 |  |
| Apple | Approach 1 |  |
| vivo | Approach 1 |  |
| OPPO | Approach 1 |  |
| Ericsson | Approach 1 |  |
| LGE | Approach 1 |  |
| CATT | Approach 1 |  |
| Nokia | Approach 1 |  |

Question 3: Is it acceptable to introduce the new field(s) into SSB-ConfigMobility in MeasObjectNR?

| Company | Yes/No | Comments |
| --- | --- | --- |
| MediaTek | Yes | Same place as legacy deriveSSB-IndexFromCell |
| Huawei, HiSilicon | Yes | Same view with MTK. |
| ZTE | Yes | Same view as MTK. |
| Samsung | Yes |  |
| Intel | Yes |  |
| Apple | Yes |  |
| vivo | Yes |  |
| OPPO | Yes |  |
| Ericsson | Yes |  |
| LGE | Yes | Same view as MTK. |
| CATT | Yes |  |
| Nokia | Yes |  |

Issue 2: Any dependency with existing field deriveSSB-IndexFromCell?

In R2-2202648 [4], it mentions that the new field is only applicable to inter-freq MOs, and the network may only indicate the field when deriveSSB-IndexFromCell is set to “true” in the same MO (means all cells on that frequency are already synchronized).

Proposal 2: The new field can be configured only if existing deriveSSB-IndexFromCell in the same MO is set to true.

Question 4: Do companies agree with the dependency between the new field(s) and the existing field deriveSSB-IndexFromCell that “The new field can be configured only if existing deriveSSB-IndexFromCell in the same MO is set to true.”

| Company | Yes/No | Comments |
| --- | --- | --- |
| MediaTek | Yes |  |
| Huawei, HiSilicon | No | The legacy field is for intra-frequency, the new field is for inter-frequency, why they are inter-dependent? If there’s no serving cell on the frequency represented by the MO, the legacy field can only be set to 0, and that’s when the new field comes into play. |
| ZTE | Yes | We want to highlight that the legacy field can be included in both intra-freq and inter-freq MOs, maybe it is clearer to look at our Rel-15 spec, or the field description of the same field in SIB4: SSB-ConfigMobility field descriptions deriveSSB-IndexFromCell If this field is set to true, UE assumes SFN and frame boundary alignment across cells on the same frequency carrier as specified in TS 38.133 [14]. Hence, if the UE is configured with a serving cell for which (absoluteFrequencySSB, subcarrierSpacing) in ServingCellConfigCommon is equal to (ssbFrequency, ssbSubcarrierSpacing) in this MeasObjectNR, this field indicates whether the UE can utilize the timing of this serving cell to derive the index of SS block transmitted by neighbour cell. Otherwise, this field indicates whether the UE may use the timing of any detected cell on that target frequency to derive the SSB index of all neighbour cells on that frequency. So if the legacy field is set to “true”, it implies all cells on that frequency are SFN/frame aligned, so the UE can first detect any cell and obtain the cell’s SSB index, then uses the same timing to derive the SSB index of other neighbour cells. That is why we think the new field is not very useful because it only saves the detection of the first cell. So when configures the new field, we think the legacy field should also be set to “true”, otherwise, they give conflicted informations (i.e. one indicates the cells are synchronized, the other does not). |
| Samsung | No | Even when the timing across different Scells are different, it could be possible for the UE to derive the timing of the inter-frequency neighbor cell based on SCellIndex. |
| Intel | Yes | Agree with ZTE |
| Apple | Tend to no, though no strong view | Even though the existing field indeed implies that the cells on that frequency is synchronized as ZTE explained, we don’t see any problem if it is set to 0 and together with the new field. We think UE can just ignore the existing field, but would not interpret it as “the cells on the frequency is non-synchronized”. |
| Intel | Yes | Agree with ZTE |
| OPPO | Yes |  |
| Ericsson | No | It appears reasonable to analyze the dependency between the two fields in the first place. Though, it seems that one should analyze the case when the legacy field is set to 0 as mentioned above by Huawei and Apple. |
| LGE |  | Both options work. We can modify the meaning of the existing deriveSSB-IndexFromCell as suggested by ZTE. In this case, the new field can be configured only if existing deriveSSB-IndexFromCell in the same MO is set to true. The alternative is we define the new field as this field indicates whether the UE may use the timing of indicated serving cell to derive the SSB index of all neighbour cells on that frequency. We slightly prefer the letter since it does not require the existing IE to be updated. |
| CATT |  | We agree with ZTE’s analysis that UE assumes SFN and frame boundary alignment across cells on the same frequency carrier if the new field is configured. Maybe we can add the similar restriction in the field description of the new field, then the dependency between the new field(s) and the existing field deriveSSB-IndexFromCell is not needed. |
| Nokia | No | Agree with Apple |

Issue 3: Whether to allow NW to indicate the new field even if the MO is regarded as intra-frequency MO

In R2-2202648 [4], it is explained that the SCell addition may change the inter-freq MO to intra-freq MO and proposes to allow NW to indicate the new field even if the MO is regarded as intra-frequency MO.

Proposal 3: Allow the network to indicate the new field even if the MO is regarded as intra-frequency MO. In this case, it is up to the UE to decide whether to use or ignore the field.

Question 5: Do companies agree with Proposal 3 in R2-2202648[4]?

| Company | Yes/No | Comments |
| --- | --- | --- |
| MediaTek | No strong view |  |
| Huawei, HiSilicon | Prefer No | The NW anyway needs to send an RRCReconfiguration to the UE, and the MO configuration can be modified. The behavior is the same for legacy UEs (the NW can set the legacy field to “1” when an inter-frequency MO becomes an intra-frequency MO). |
| ZTE | Yes | The network can update MO configuration by RRCReconfiguration, but this results in measurement refresh (e.g. reset TTT) on that frequency. So we think the proposal is useful to void MO reconfiguration, this is similar to the handling of “measCycleSCell” that the field can be configured even if SCell is not configured. |
| Samsung | No | This is an optimization. We prefer a cleaner solution though we understand there can be small drawbacks. |
| Intel | No | This seems like an optimization. We also prefer not to introduce it at this stage. |
| Apple | No | This is indeed an optimization. |
| vivo | No |  |
| OPPO | No |  |
| Ericsson | No |  |
| LGE | No | It is natural the NW modifies it to intra-frequency MO when a cell on that frequency becomes an SCell. |
| CATT | No strong view |  |
| Nokia | No |  |

Issue 4: Whether to enable SSB derivation of SSB indexes of target cell on inter-frequency from serving cell timing for the target frequency to measure in idle/inactive state (in SIB4/RRCRelease message)

In addition to MesObjectNR, R2-2203503 [11] proposes to also introduce the same new field(s) to SIB4 and MeasIdleConfig in RRCRelease message.

Question 6: Do companies agree to introduce the same new field(s) into SIB4, and MeasIdleConfig in RRCRelease message, to enable derivation of SSB indexes of target cell on inter-frequency from serving cell timing for the target frequency to measure in idle/inactive state?

| Company | Yes/No | Comments |
| --- | --- | --- |
| MediaTek | No | Extend this to IDLE/INACTVE mode is not related to NCSG at all. We prefer no further optimization. |
| Huawei, HiSilicon | No | This does not look essential. |
| ZTE | No strong view |  |
| Samsung | No | In idle state, there is no SCell. In Inactive SCells may be stored, but there is no motivation to introduce. Besides, RAN4 clearly indicated that the indication can be per MO. |
| Intel | No |  |
| Apple | No | Extension of the feature use case would better come from RAN4. |
| vivo | No |  |
| OPPO | No | Out of the WI scope. |
| Ericsson | No |  |
| LGE | No | The NCSG is not used in IDLE/INACTIVE. |
| CATT | No |  |
| Nokia | No |  |

## Open issue N1-7: NCSG reporting is independent from or combined with Rel-16 NeedForGap reporting

Issue 1: Independent or combined with Rel-16 NeedFroGap reporting

In R2-2203713 [1], the following summary and proposal is provided by the moderator.

Summary: 9/10 companies support independent reporting of NCSG from Rel-16 NeedForGap reporting. 1/10 company supports combined signaling. Proposal 3: Support independent Rel-17 NCSG reporting from Rel-16 NeedForGap reporting.

Question 7: Do companies agree to support independent Rel-17 NCSG reporting from Rel-16 NeedForGap reporting?

| Company | Yes/No | Comments |
| --- | --- | --- |
| MediaTek | Yes |  |
| Huawei, HiSilicon | Yes |  |
| ZTE | Yes |  |
| Samsung | Yes |  |
| Intel | Yes |  |
| Apple | Yes |  |
| vivo | YES |  |
| OPPO | Yes |  |
| Ericsson | Yes | Given the online agreements we can compromise here. |
| LGE | Yes |  |
| CATT | Yes |  |
| Nokia | Yes |  |

Issue 2: Allow simultaneous configuration on Rel-16 NeedForGap and Rel-17 NCSG?

R2-2202648 [4] has the following proposal. The motivation is mainly for mobility, i.e, source cell can transfer both Rel-16 NeedForGap capability and Rel-17 NCSG capability to target cell. If Target cell is of version Rel-16, it can benefit from acquiring the Rel-16 NeedForGap information.

Proposal 6: Network can enable R16 NeedForGap and R17 NeedForNCSG capability reporting at the same time, it is up to UE to ensure the reported gap requirements are compatible.

Question 8: Do companies agree to support simultaneous configurations on Rel-16 NeedForGap and Rel-17 NCSG?

| Company | Yes/No | Comments |
| --- | --- | --- |
| MediaTek | See comment | If independent reporting (issue 1) is agreed, we don’t see much need to report the duplicating information. But we are fine if majority prefer to support this. For handover scenario, maybe R17 gNB could derive R16 information from R17 IE and send both R16/R17 information to target. |
| Huawei, HiSilicon | No | We don’t see the benefit of duplicated reporting. Besides, the R16 NeedForGap reporting does not work well, there has been discussion in TEI16 in RAN4 on whether “no-gap” in Rel-16 NeedForGap signalling allows for interruption or not, but no conclusion was reached. |
| ZTE | Yes | We think the UE needs to follow the configuration from network, there seems no benefit to disallow such flexibility. Regarding MTK’s comments, it requires extra effort to ‘translate’ the capability at network side upon handover procedure. |
| Samsung | Yes |  |
| Intel | No | It seems like an optimization. We think that if Rel16 gNB can’t understand, MT solution will work base on network implementation instead of redundant information from the UE. |
| Apple | No strong view | From ASN.1 signaling wise, we don’t think there is a need to restrict that NeedForGap and NCSG can not be configured together, nor a need to explicitly mention the simultaneous configurations. So nothing needs to be done on this matter. |
| vivo | Yes |  |
| OPPO | Yes |  |
| Ericsson | No | As per issue’s 1 (Q7) evident outcome |
| LGE | Yes | If it is not needed, NW will not configure both simultaneously. No reason to prohibit it from signalling perspective. |
| CATT | No | We don’t see the benefit of duplicated reporting. We wonder if the target gNB can configure Rel-16 NeedForGap after HO. |
| Nokia | No | NW implementation can handle the case. No need to ask UE report duplicate information. |

Issue 3: Inter-node signaling

R2-2202945 [7] proposes to introduce the Rel-17 NCSG requirement information in HandoverPreparationInformation inter-node message.

Proposal 3: R17 NCSG requirement information is introduced in HandoverPreparationInformation inter-node message.

Question 9: Do companies agree with Proposal 3 in R2-2202945?

| Company | Yes/No | Comments |
| --- | --- | --- |
| MediaTek | Yes | Similar to R16 |
| Huawei, HiSilicon | Yes |  |
| ZTE | Yes |  |
| Samsung | Yes |  |
| Intel | Yes |  |
| Apple | Yes |  |
| vivo | Yes |  |
| OPPO | Yes |  |
| Ericsson | Yes |  |
| LGE | Yes |  |
| CATT | Yes |  |
| Nokia | Yes |  |

# Conclusion

[TBA]