3GPP RAN WG2 Meeting #117	R2-220xxxx
eMeeting, February 21st – March 4th, 2022

Agenda Item:	8.6.2

Source:	InterDigital (rapporteur)

Title:	Summary of remaining user plane issues for SDT

Document for:	Discussion, Decision

# Introduction

This is the summary report for tdocs submitted to the UP SDT agenda item 8.6.2 and for offline discussion 502:

[AT117-e][502][Sdata] UP additional open issues (InterDigital) Remaining UP open issues Deadline: Proposals by rapporteur by Friday (intermediary deadlines for comments to be set by rapporteur) Deadline for companies inputs: Thursday, Feb 24th, 20:00 UTC Draft proposals ready by Friday, Feb 25th, 2:00 UTC Proposals ready by Friday, Feb 25th, 23:59 UTC

Given the following guidance was issued for the agenda item:

Including email discussion [POST116bis-e][510][Sdata] UP open issues (Huawei) – NO contributions on these issues.

Any other contributions should focus on important issues not covered by open issues email discussions. Issues that have been discussed and not agreed in the past should not be brought again, unless there is large support (i.e. large number of companies co-sourced contributions)

the summary is categorized by the following:

- Remaining open issues: 
Solutions for the issue is proposed by more than one company not covered by the pre-meeting email discussion; the issue can be important for R-17 completion. This is the focus of this discussion document.

- Issues already addressed by pre-meeting discussions:
Issue is addressed by in the pre-meeting email discussion or have been discussed in the past and not agreed. Companies are not expected to provide input on such issues unless the chair indicates the need for further offline discussion.

- Non-critical issues: 
The issue is non-critical for R17 completion or proposed by a single company. Companies should not provide input on it, unless they think issue is important to be addressed in rel-17. If you are not supporting, no need to respond. A proposal will be produced by the rapporteur to support the issue only if there is considerable support expressed in this discussion.

# Remaining open issues

## General UP issues

### SR and BSR

It was agreed to use the default MAC cell group configuration for BSR. The SRB default configuration has a single default LCG (LCG 0) assigned to SRB LCHs, while the default MAC cell group configuration doesn’t specify anything for LCG for DRBs. The following options for the default LCG assignment for LCHs of SDT DRBs are proposed:

- Option 1: LCG 0 is also used for DRBs configured for SDT. This results in using short BSR MAC CE for SDT and bundling buffer status for SDT DRBs and DRBs. [11]

- Option 2: A dedicated LCG ID (e.g., LCG 1) is used by default for DRBs configured for SDT. This results in using a long BSR MAC CE and separating buffer status reporting for SDT DRB buffered bits. [9, 11]

Question 1: which of the above options for the default LCG assignment for SDT DRB LCHs do you prefer?

| Company | Preferred option | Additional comments |
| --- | --- | --- |

In RAN2#116bis-e, it was agreed that “LCH SR delay timer is supported and configurable by SIB.  All logical channels configured with SDT are configured with a same timer value. The logicalChannelSR-Mask is supported.” [11] suggests to further clarify that the value of the LCH SR mask should be set to true for all SDT LCHs, as the intention is to prevent the triggering of SR or RA-SR from those LCHs while the timer is running.

Question 2: Do you agree to clarify in TS 38.331 that logicalChannelSR-Mask value is set to true for all LCHs of DRBs configured for SDT?

| Company | Answer | Additional comments |
| --- | --- | --- |

### Switching from RA-SDT to non-SDT resume

Switching from SDT to non-SDT was already agreed based on network signalling (e.g. RRC resume message). An FFS is whether we additionally allow UE autonomous switching, e.g. in scenarios where the network fails to decode the SDT payload. [3, 7, and 8] proposes to allow the UE to switch from RA-SDT to normal RACH if the initial transmission has been failed for a configured number of times. The alternative is to rely on the SDT failure timer for handling the SDT TB. [3] recognize that this may require msg3/A rebuilding, and thus suggest supporting a separate Msg3/A PUSCH buffer configured solely for RA-SDT.

Question 3: Do you support UE-autonomous switching from RA-SDT to normal RACH if the initial transmission fails a configured number of times?

| Company | Answer | Additional comments |
| --- | --- | --- |

### RA timers

[5, 7] proposes to allow configuration of longer values of ra-ContentionResolutionTimer and msgB-ResponseWindow for small data transmission as compared to legacy RACH. The benefit is to allow for longer processing time for Msg3 and MsgB payloads, similar to EDT. [7] further proposes to introduce an offset for the start of the response window for RA-SDT, for power savings reasons.

Question 4: Do you agree to introduce larger configuration values of ra-ContentionResolutionTimer and msgB-ResponseWindow for SDT or a starting offset?

| Company | Answer | Additional comments |
| --- | --- | --- |

## CG-SDT issues

### SSB selection for subsequent SDT

It was agreed that for subsequent new CG transmissions, the UE re-evaluates the SSB for the purpose of CG resource selection. It is FFS what happens if no SSBs are valid or if no sample is available. In the case there are no SSBs available for subsequent TBs, the following options are possible:

- Option 1: Follow earlier agreement: UE falls back to legacy RA: 

“During subsequent CG transmission phase (i.e. after the UE has received response from NW) UE can initiate at least legacy RACH procedure (e.g. trigger due to no UL resources).  No MAC PDU rebuilding is required.  At least the following conditions are agreed: (1) no qualified SSB when the evaluation is performed; (2) when TA is invalid; (3) when SR is triggered due to lack of UL resource”

- Option 2: Follow earlier agreement: UE falls back to legacy RA, but only if PHY layer informs MAC there is no SSB above the RSRP threshold [3]. Specify interaction between PHY and MAC.

- Option 3: When there is no SSB sample in the CG occasion enough to be evaluated, the last selected SSB is reused for the subsequent CG-SDT transmission [7, 11]. Subsequent SDT data is transmitted on CG.

Question 5: In case there is no available SSB above the configured RSRP threshold, which of the above options do you prefer for the transmission of the subsequent SDT data?

| Company | Preferred option(s) | Additional comments |
| --- | --- | --- |

In the case there is at least one SSBs available for subsequent TBs in a CG-SDT session, the following options are possible:

- Option 1: if the last previously selected SSB for CG-SDT is valid (RSRP above threshold), the last selected SSB is reused for the next CG-SDT transmission (even if there is a better SSB). UE selects another SSB if the last SSB is not valid [11].

- Option 2: The UE may select another SSB only if a configuration is configured by the network to allow this autonomous reselection by the UE (even if another SSB has higher RSRP) [11].

- Option 3: Up to UE implementation to select an SSB above the RSRP threshold for the CG-SDT resource.

Question 6: In case there is at least one SSB above the configured RSRP threshold, which of the above options do you prefer for SSB selection for subsequent CG-SDT TBs? Multiple can be selected

| Company | Preferred option(s) | Additional comments |
| --- | --- | --- |

### Legacy RA following CG-SDT

It has been agreed that the UE switches to regular legacy RA upon data arrival in the subsequent SDT phase, when the UE does not have a valid grant, TA is invalid, or if there isn’t any SSB to select for subsequent SDT. For such RA initiated following CG-SDT, [3, 7] suggest that the UE includes only the C-RNTI MAC CE -potentially with a BSR- instead of RRC resume request CCCH message in the payload of Msg3/A.

Question 7: For RA initiated after CG-SDT, do you agree that RRC resume request should not be included in Msg3/A and instead a C-RNTI MAC CE is multiplexed?

| Company | Answer | Additional comments |
| --- | --- | --- |

### UE behaviour upon expiry of CG-SDT-TAT

It was agreed that upon expiry of CG-SDT-TAT, the UE should clear all SDT configured grant, flushes HARQ buffer and continue to maintain NTA. While the CG-SDT procedure is ongoing, CG-SDT-TAT can expire, possibly before the UE has received any response from the network. The following proposals are made for the UE behaviour when CG-TAT expires:

- Option 1: If CG-SDT-TAT expires while the CG-SDT procedure is ongoing and if UE has not received a response after the initial UL CG-SDT transmission, UE terminates ongoing SDT procedure [2].

- Option 2: If CG-SDT-TAT expires while the CG-SDT procedure is ongoing and if UE has not received a response after the initial UL CG-SDT transmission, UE initiates RA-SDT transmission [12].

- Option 3: Modify earlier agreement on flushing HARQ buffer upon expiry [1]:
Flush HARQ buffers only if both legacy TAT and CG-TAT expire. If TAT is running, UE does not clear all the HARQ buffers when CG-SDT-TAT expires. The rapporteur understands that this scenario does not happen due to agreements made this meeting:

  - CG-SDT resources are not used during an RA-SDT. Consider the CG-SDT-TAT as expired at the initiation of an RA-SDT procedure

  - UE stops the legacy TAT when contention resolution is successful for RACH triggered during CG-SDT

- Option 4: Other or none (e.g. rely on SDT failure timer to terminate the SDT procedure).

Question 8: Which of the above options do you prefer for the UE behavior upon expiry of CG-TAT? Multiple can be selected

| Company | Preferred option(s) | Additional comments |
| --- | --- | --- |

# Open issues already addressed by other discussions

### Issues indicated for need of further offline discussion

#### UE behaviour upon reaching preambleTransMax in RA-SDT

As explained in section 2.1.2, Switching from SDT to non-SDT was already agreed based on network signalling (e.g. RRC resume message). The pre-meeting email discussion [4] discusses the UE behaviour upon reaching preambleTransMax for a RA-SDT procedure in INACTIVE state. The following options are expressed:

- Option 1: As in legacy, MAC entity indicates to RRC the Random-Access problem (max preamble transmission is reached) and the RA procedure continues. UE remains in INACTIVE until the SDT failure timer expires. No new indication to RRC indication is specified and no action is specified in RRC. 

This is in line with P8 from the pre-meeting CP issues email discussion [17]:
Proposal 8: RLC failure handling needs to be added in RRC but Max RACH preamble transmission indication from lower layers leads to no response in RRC (same as legacy).

- Option 2: Same as option 1, but RRC initiates legacy RRC resume procedure after receiving a Random-Access problem notification from MAC if the RA procedure was initiated for SDT by RRC.

- Option 3: Specify a new notification to RRC of SDT failure when the number of preamble transmission in RA-SDT exceeds the threshold preambleTransMax. RRC initiates an RRC resume procedure after receiving this notification of SDT failure from MAC.

It was also discussed online that a first TB transmitted by RA-SDT is initiated by RRC. For subsequent SDT TBs for CG-SDT and RA-SDT, the RA-SDT procedure may be initiated by the MAC layer. An initial discussion occurred online, and further discussion is left for this offline: =>	cover this issue in UP email discussion

Question 9: For a RA-SDT initiated for the transmission of a first SDT TB, which of the above options do you prefer for the UE behavior upon reaching preambleTransMax?

| Company | Preferred option | Additional comments |
| --- | --- | --- |

Question 10: For a RA-SDT initiated for the transmission of subsequent SDT, which of the above options do you prefer for the UE behavior upon reaching preambleTransMax?

| Company | Preferred option | Additional comments |
| --- | --- | --- |

#### RB handling upon reception of RRC message:

It was agreed that for both DRBs and SRBs configured with SDT, the UE autonomously re-establishes RLC entities for both DRBs and SRBs upon reception of RRCRelease message. Regarding the FFS on PDCP discard for SRBs, [6, 9] proposes to discard PDCP SDUs of SRBs upon reception of RRCRelease message with suspendConfig. This topic was addressed by the premeeting email discussion [4]. The following options were discussed:

- Option 1: Leave it to UE implementation that the old SRB data are not counted in the data volume calculation

- Option 2: UE performs SDU discard at the reception of RRCRelease with SDT configuration.

After a brief online discussion, it was mentioned that option 2 can be assumed and further discussion can be made in this offline. The intention after all is to not include old PDCP SDUs for SRB (SDUs arrived before RRCRelease reception) in the SDT data volume calculation.

Question 11: Do you agree that the UE performs SDU discard at the reception of RRCRelease with SDT configuration?

| Company | Answer | Additional comments |
| --- | --- | --- |

[5] addresses the FFS on the UE behaviour upon reception of RRC Reject; [5] proposes to suspend all the RBs/PDCP entities configured for SDT and re-establish corresponding RLC entities upon reception of RRC reject. This issue is to be handled in the AT meeting CP offline discussion.

### Remaining open issues from the MAC running CR

UE behaviour upon expiry of configuredGrantTimer

This issue (L308) was flagged to be discussed in this offline. If the UE initiates the CG-SDT procedure and does not receive confirmation of initial CG-SDT transmission from the network before the CGT expiry, what is the expected UE behaviour?

- Option 1: as in legacy, the UE flushes the HARQ process buffer upon expiry ConfiguredGrantTimer, e.g. the UE can perform a new subsequent SDT transmission on the same HARQ process after CGT expiry.

- Option 2: The UE triggers SDT failure procedure upon CGT expiry. This may be redundant, as we already have the SDT failure timer.

In case the transmission was successfully received by the NW, it’s likely that the UE has received a NW response before the expiry of CGT. UE may then reuse the HARQ process for subsequent small data if needed, following the reception of the reception of confirmation of initial transmission from the gNB, as agreed. In case no response was received from the NW for initial CG-SDT transmission, the UE keeps retransmitting the TB after expiry of the cg-retransmission timer until the CGT expires or until the SDT failure timer expires. It is therefore expected that the legacy behaviour (option 1) is sufficient, and no need to specify anything in addition.

Question 12: Do you agree that, as in legacy, the UE flushes the HARQ process buffer upon expiry ConfiguredGrantTimer? No special UE handling is required

| Company | Answer | Additional comments |
| --- | --- | --- |

Reference RSRP value for RSRP-based TA validation

The issue (L317) was flagged to be discussed in this offline. It was agreed this meeting that “Downlink RSRP reference at the time of receiving RRCRelease with suspendConfig for the RSRP-based TA validation is determined by the MO configured for the cell where the UE is released from RRC_CONNECTED to RRC_INACTIVE.”

In the MAC running CR [18], the reference RSRP value is obtained when the MAC entity last resets. However, it is not clear when the MAC entity last resets and whether that is the same as the time instance when RRCRelease with suspendConfig  is received. The following options are possible to capture the agreement in TS 38.321:

- Option 1: keep modelling in the running CR [18]: reference value determined when “MAC entity last resets”

The MAC entity shall consider the TA of the initial CG-SDT transmission with CCCH message to be valid when the following conditions are fulfilled: 1> compared to the downlink pathloss reference RSRP value when the MAC entity last resets for initial CG-SDT transmission with CCCH message, the RSRP has not increased/decreased by more than cg-SDT-RSRP-ChangeThreshold, if configured.

- Option 2: Use: “compared to the downlink pathloss reference RSRP value when the CG-SDT resource is configured by upper layers”

The MAC entity shall consider the TA of the initial CG-SDT transmission with CCCH message to be valid when the following conditions are fulfilled: 1> compared to the downlink pathloss reference RSRP value when the CG-SDT resource is configured by upper layers, the RSRP has not increased/decreased by more than cg-SDT-RSRP-ChangeThreshold, if configured.

- Option 3: Use: “compared to the downlink pathloss reference RSRP value when the RRCRelease with suspendConfig is received by upper layers”

Question 13: which of the above options do you prefer to capture the agreement on reference RSRP value for RSRP-based TA validation?

| Company | Preferred option | Additional comments |
| --- | --- | --- |

### Other issues

CG-SDT-TAT handling

It was agreed that the UE maintains a single NTA, regardless of whether legacy TAT, CG-SDT-TAT, or both are running. [8] suggests that both timers should not operate both timers simultaneously, and thus suggests to stop CG-SDT-TAT when the legacy TAT is started.

[14] also proposes to not use CG-SDT resources while RA-SDT session is ongoing (even when the CG-SDT configuration may be valid), upon initiation of a RA-SDT session.

During the online session this meeting, it was agreed that:

- CG-SDT resources are not used during an RA-SDT. Consider the CG-SDT-TAT as expired at the initiation of an RA-SDT procedure

- UE stops the legacy TAT when contention resolution is successful for RACH triggered during CG-SDT

The rapporteur understands that with those agreements, the proposals in [8] and [14] are already addressed.

| Company | Add comments only if you think there is further clarification needed |
| --- | --- |

SP-SRS (de)activation during SDT

It was agreed in the positioning work item that semi-persistent positioning SRS Activation/Deactivation MAC CE is reused for triggering SRSp transmission in RRC_INACTIVE. This issue is discussed in discussion [15] -ref to P4-, whereby the MAC CE can be sent in an SDT session either along with the RRC Release message or in a later DL TB. [14] proposes to confirm the understanding that this MAC CE can be received during an SDT session, e.g. by providing positioning reconfiguration via Msg4/B along with RRCRelease in response to the transmission of the SDT payload.

CG configuration request:

In addition to BSR reporting, [11] proposes allow the UE to include a to request to the network for a pre-configured PUSCH based SDT resource/configuration. This has been discussed in multiple past email discussions on CG-SDT without consensus. [11] also proposes to allow the UE to indicate to the Network its preferences in regard to the time occurrence of the CG-SDT occasion.

Order between carrier and PRACH partition selection

Whether a carrier is selected before RACH partition or not is discussed in the UP RA partitioning premeeting email discussion [13]. [5] proposes to select the carrier after RACH partition selection, as SDT as an SDT-specific RSRP carrier selection threshold.

# Non-critical issues

### Rebuilding of the initial CG-SDT TB to update BSR

It’s been agreed that the UE retransmits the initial TB transmitted on the CG-SDT after expiry of the cg-SDT-retransmisisonTimer if there was no response received from the network (e.g. DG or a subsequent DL transmission). [10] proposes to allow the UE to rebuild the TB upon transmitting it again on CG-SDT, for the benefit of updating the BSR MAC CE to accurately reflect new data that may have arrived since the initial TB was constructed. [10] also suggests adding the following note into TS 38.321:

NOTE 5:	If a HARQ process is configured with cg-RetransmissionTimer and if the BSR is already included in a MAC PDU for transmission by this HARQ process, but not yet transmitted by lower layers, it is up to UE implementation how to handle the BSR content.

| Company | Add comments only if you support resolving this proposal in Rel-17 and why |
| --- | --- |

## LCP

SDT vs. non SDT DRB determination based on LCP restrictions

[11] suggests that SDT DRBs that cannot be multiplexed on SDT resources available in the current SDT procedure due to LCH restrictions (e.g. CG resource restrictions) should be considered as non-SDT DRBs for the duration of the SDT procedure. This may end up restricting the scheduler from using a dynamic grant to accommodate data from those SDT DRBs, and also results in not allowing data transmission from those DRBs using RA-SDT.

| Company | Add comments only if you support resolving this proposal in Rel-17 and why |
| --- | --- |

Handling of Bj

[3] suggest to optimize the handling of Bj in Inactive state, such that the UE does not update nor increase Bj while in Inactive state, i.e. between the reception time of RRC release message and the initiation of the SDT procedure. The benefit is to avoid starting the LCP procedure with high values for Bj at the time of SDT initiation.

| Company | Add comments only if you support resolving this proposal in Rel-17 and why |
| --- | --- |

### Switching from CG-SDT to RA-SDT

One open issue is whether to allow switching from CG-SDT to RA-SDT for the initial CG-SDT TB. [7] proposes to allow the UE to switch to RA-SDT (if the RA-SDT criteria is met) when the initial TB is not successfully transmitted in the initial phase of CG-SDT. However, it was already agreed that the UE retransmits the initial CG-SDT TB after expiry of the cg-SDT-retransmissionTimer. This proposal seems to conflict with this this behaviour already captured in the running MAC CR.

| Company | Add comments only if you support this proposal in Rel-17 and why |
| --- | --- |

### TA maintenance based on DL timing

In addition to maintaining timing advance based on TA commands and RSRP change for CG-SDT, [3] suggests to also maintain uplink timing alignment by gradually adjusting uplink timing when there is a DL timing difference from the DL timing reference observed by the UE, similar to connected mode.

| Company | Add comments only if you support this proposal in Rel-17 and why |
| --- | --- |

### Carrier re-selection for subsequent CG-SDT

[1] proposes to re-evaluated the selected uplink carrier (NUL vs. SUL) for each subsequent TB transmitted on CG-SDT resources. The running CR already suggest that the selected carrier selected for the initial CG-SDT transmission is not changed for subsequent TBs.

| Company | Add comments only if you support this proposal in Rel-17 and why |
| --- | --- |

### Power ramping for CG-SDT

[8] proposes to support power ramping for CG-SDT retransmissions, i.e. after the expiry of the cg-SDT-retransmissionTimer, similar to power rmaping in the RA procedure.

| Company | Add comments only if you support this proposal in Rel-17 and why |
| --- | --- |

# Conclusion

RAN2 should discuss the above and agree to the following:

TBD

# References

R2-2202274, Discussion on user plane issues of SDT, OPPO

R2-2202342, CG-SDT-TAT expiry handing during the CG-SDT procedure, Samsung Electronics Co., Ltd

R2-2202446, Remaining UP issues for SDT,	Lenovo, Motorola Mobility

R2-2202609, Summary of [POST116bis-e][510][Sdata] UP open issues (Huawei), Huawei, HiSilicon

R2-2202610, Remaining issues for SDT user plane	, Huawei, HiSilicon

R2-2202735, Remaining issues of user plane aspects of SDT, China Telecom

R2-2202959, Remaining issues on UP aspects of SDT, Qualcomm Incorporated

R2-2202983	, Remaining UP Issues on SDT Procedure, vivo

R2-2203008, Remaining user plane aspects of SDT, NEC

R2-2203158, User Plane Aspects for SDT, Ericsson

R2-2203280, UP and CG aspects for SDT, Nokia, Nokia Shanghai Bell

R2-2203458, Remaining UP issues for SDT, InterDigital

R2-2203309, [POST116bis-e][514][RA Part] - Open issue list summary, ZTE Corporation (rapporteur)

R2-2202674, Additional discussion on identified open CP issues	, Intel Corporation

R2-2203524, Email discussion Report on [Pre117-e][609][POS] Open issues on positioning in RRC_INACTIVE, InterDigital

R2-2202609, Summary of [POST116bis-e][510][Sdata] UP open issues (Huawei), Huawei, HiSilicon

R2-2203716, [POST116bis-e][511][Sdata] - CP open issue list summary, ZTE Corporation (rapporteur)

R2-2202611, Introduction of Small Data Transmission for MAC spec, Huawei, HiSilicon