## Slide 1: [508]

## Slide 2: [AT121][508][V2X/SL] COT usage scenario and LCP enhancement (OPPO)
Scope: Clarify the COT usage scenarios (excluding reception of multiple COTs) and discuss how to handle each scenario (including LCP enhancement on L2 destination id and/or CAPC restriction). With consideration of RAN1 agreements.
Intended outcome: Discussion summary in R2-2302035
Deadline: Comeback at 3/3 CB session

## Slide 3: Background
Proposal 3 In the LCP procedure, the responding UE considers the COT info (i.e., including whether the selected Destination is associated with the COT initiating UE and CAPC value).
[LG]: Support the proposal. Minimum change of LCP is required to use COT (based on RAN1 agreements). [Xiaomi]: For L2 destination id aspect, it is still FFS in RAN1. For CAPC aspect, we can consider alternative solution (e.g. assistance information is provided by responding UE to initiating UE, the initiating UE assigns based on the received information, then we may not need LCP change in the responding UE when COT is used). [Ericsson]: L2 destination id restriction is clear at least for UC (to RAN1 agreement). [Lenovo]: Support the proposal. [Vivo]: It is similar to a NR-U case where DCI indicates CAPC value, but in NR-U there was no change of LCP due to that. [Huawei, Lenovo]: It was not specified because it was clear requirement. Also it is for mode 1 operation, so the gNB is well aware of the status of the UE. [LG]: Compared to NR-U, in SL-U LCP has a L2 destination id selection. [OPPO]: Companies may want to see whole cases and see the solution for each case.

## Slide 4: Observation
It seems there would be anyway some cases where the COT cannot be used, (e.g., 1/ MAC PDU generated before COT arrival which does not satisfy the COT requirement, or 2/ MAC PDU has not been generated but no data in RLC buffer satisfying COT requirement and etc.)
It seems there would be anyway cases where the COT can be used (e.g., if following legacy LCP, the generated MAC PDU already satisfies the COT requirement)

## Slide 5: Observation
The key issue seems for the case where
1) If following legacy LCP (no change), the generated MAC-PDU does not satisfy the COT requirement
2) Yet if change LCP a bit (destination-selection and/or LCH-selection), the generated MAC-PDU can satisfy the COT requirement
What the UE should do

## Slide 6: Observation: Solutions on the table
Solution-1: Make use of the COT (i.e., type-2 LBT) + an improved LCP to ensure MAC-PDU satisfy the COT requirement
Solution-2: Not make use of the COT, but rely on type-1 LBT, and rely on the legacy LCP change

## Slide 7: Q: How do we proceed
Unless we identify infeasibility of solution-1 and/or solution-2
Way-out-A: trying to down-select between the 2 solutions
Way-out-B: trying to allowing both, and up to UE to select which solution to use

## Slide 8: Recommended WF