## Slide 1: Offlien-429 Summary
Apple
R2-2311392

## Slide 2: Introduction
[AT123bis][429][Relay] Remaining proposals from path addition/change discussion (Apple)
Scope: Discuss the remaining proposals from R2-2310350, and P3 of R2-2310781, and attempt to converge.
Intended outcome: Report to Thursday CB session in R2-2311392
Deadline: Thursday 2023-10-12 1100 CST
Schedule: Wednesday 2023-10-11 1600-1700 (not using Brk3, discussion in coffee break space)

## Slide 3: Really easy?
[Easy]Proposal 14: [20/20] PC5-RRC trigger is NOT to be used when (the duplicated) RRCReconfiguraitonComplete is sent via indirect path.
[Easy]Proposal 15: [19/20] The start condition of new T420-like timer is “Upon reception of the RRCReconfiguration message including sl-IndirectPathAddChange”.
[Easy]Proposal 23: [19/19] For path addition/change cases in MP Scenario 1, RRCReconfgurationComplete is always transmitted in direct path. Only if NW configures split SRB1 with PDCP duplication, RRCReconfigurationComplete message is sent to gNB via both paths.

## Slide 4: Related to morning agreement:
Morning agreement:
  At T304 expiry in direct path addition/change, the remote UE triggers re-establishment, indicating the source cell as the PCell before the path addition/change. FFS if any spec impact over legacy operation.
[To discuss]Proposal 6: Upon T304 expiry for direct path addition/change, RRC reestablishment is always triggered w/o any condition (11/18)[WA]
or only when SRB1 in indirect path not configured/suspended (7/18).

## Slide 5: Key Issue : T420-stop condition
[To discuss]Proposal 16: [10/20] The T420-like timer stop condition of IDLE/INACTIVE relay case depends on whether RRCReconfguraitonComplete is sent via indirect path or not, assuming legacy Rel-17 T420 condition can be reused if yes.
[To discuss]Proposal 17: [13/20] Dowon-select one of the following for the T420-like timer stop condition of IDLE/INACTIVE relay addition/change (at least for the case that RRCReconfguraitonComplete is not sent via indirect path):
- Option 1: upon PC5-RRC connection establishment
- Option 2: Upon PC5 RLC acknowledgement of the PC5-RRC message triggering relay UE entering CONNECTED state
- Option 3: upon reception of RRCReconfigurationCompleteSidelink
[To discuss]Proposal 18: RAN2 to discuss whether the T420-like timer stop condition of CONNECTED relay case is as same as legacy Rel-17 T420 stop condition (11/20) or same as condition(s) in IDLE/INACTIVE case, if applicable.

## Slide 6: Discussion:
Discuss a simplified solution:
  R17 Legacy T420 stop condition if RRCRecnfigComplete is transmittged in indirect path(i.e., PC5 RLC ACK of RRCReconfigurationComplete in indirect path)
  Else,down-select from the following:
    Option 1: PC5 RLC ACK of PC5-RRC triggering message
    Option 2: PC5- connection is established (i.e., PC5-S procedure is complete) .
    Option 3: upon reception of RRCReconfigurationCompleteSidelink

## Slide 7: Key Issue : At the expiry of T420
[Easy]Proposal 19: [15/19] The remote UE falls back to the configuration/operation prior to indirect path addition/change at the expiry of new T420-like timer. FFS whether/how to handle the path change case that the prior indirect path is released before the T420 expiry.
[Easy]Proposal 20: [15/19] The remote UE reports the failure of indirect path addition/change to gNB at the expiry of T420-new like timer.
[Easy]Proposal 22: [14/19] The remote UE may not initiate RRC reestablishment procedure upon the expiry of new T420-like timer. FFS whether this is conditional on the availability of SRB1 in direct path.
Proposal 21: [10/15] If indirect path add/change failure is to be reported, at least include the indication of failure. FFS which message is used. and the reason causing the indirect path failure in the report (assuming indirect path failure is implicitly or explicitly indicated by the report message) .

## Slide 8: Discussion proposals T420 expiry:
Option 1: Fallback + RRCRestablishment (legacy MCG failure)
  Nokia,
Option 2: Failure report only
  Huawei,QC,Lenovo, OPPO,LG,vivo,Xiaomi,CATT,CT,E///
Option 3: Fallback to prior config + Failure report
  ZTE,

## Slide 9: Key Issue: Handle relay UE ”wrong cell”
[To discuss]Proposal 8: [10/20] RAN2 to discuss whether/how to avoid/handle the case when the target L2 MP Relay UE establishes a RRC connection with a different gNB than the gNB serving the target cell.
[To discuss]Proposal 9: [10/10] If the error case in P8 is to be addressed, remote UE reports the “wrong gNB” failure to PCell after the failure is detected. FFS how remote UE detects this failure (e.g., differentiate this case with the case that relay UE reselects another cell under the same gNB).

## Slide 10: Discussion
Try for a minimum behavior:
  On top of Rel 17 solution.
  FFS how remote UE handle this instead of initiating RRCreestablisment?
  No conclusion. Remaining open Issue

## Slide 11: Key Issue: Rel-17 Relay
Proposal 3: RAN2 discusses whether Rel-17 Relay UEs can be considered as candidate target Relay UEs.

## Slide 12: Discussion
Consider following options if we want to support R17 Relay:
  Option 1: R18 relay UE indicates “R18/Pc5-rrc trigger support” in PC5 discovery message for the purpose of MP support. (QC,HW,CMCC,CATT)
    Concern： UE capability exposed in PC5 before unicast link established
  Option 2：leave it to NW implementation (OPPO,IDC,ZTE,
Open Issue

## Slide 13: Conclusions (1): to be agreed
Proposal 1: PC5-RRC trigger is NOT to be used when (the duplicated) RRCReconfigurationComplete is sent via indirect path.
Proposal 2: The start condition of new T420-like timer is “Upon reception of the RRCReconfiguration message including sl-IndirectPathAddChange”.
Proposal 3: For path addition/change cases in MP Scenario 1, RRCReconfgurationComplete is always transmitted in direct path. Only if NW configures split SRB1 with PDCP duplication, RRCReconfigurationComplete message is sent to gNB via both paths.
[Working assumption] Proposal 4:Upon T304 expiry for direct path addition/change, RRC reestablishment is always triggered w/o any condition
Proposal 5: If RRCReconfigurationComplete is transmitted in indirect path, reuse R17 Legacy T420 stop condition (i.e., PC5 RLC ACK of RRCReconfigurationComplete in indirect path) for new T420-like timer. Else, down-select from the following options for the stop condition:
  Option 1: PC5 connection is established (i.e., PC5-S unicast link establishment procedure is complete) .
  Option 2: upon reception of RRCReconfigurationCompleteSidelink
Proposal 6: The remote UE reports the failure of indirect path addition/change to gNB at the expiry of new T420-like timer.
Proposal 7: If indirect path add/change failure is to be reported, at least include the indication of failure. FFS which message is used.

## Slide 14: Conclusion (2)
To be discussed (Remaining Open issue):
  Proposal 8: RAN2 to discuss whether/how to avoid/handle the case when the target L2 MP Relay UE establishes a RRC connection with a different gNB than the gNB serving the target cell.
  Proposal 9: If the error case in P8 is to be addressed, remote UE reports the “wrong gNB” failure to PCell after the failure is detected. FFS how remote UE detects this failure (e.g., differentiate this case with the case that relay UE reselects another cell under the same gNB).
  Proposal 10: RAN2 discusses whether Rel-17 Relay UEs can be considered as candidate target Relay UEs.

## Slide 15: Annex: Remaining Proposals in R2-2310350
[Easy]Proposal 14: [20/20] PC5-RRC trigger is NOT to be used when (the duplicated) RRCReconfiguraitonComplete is sent via indirect path.
[Easy]Proposal 15: [19/20] The start condition of new T420-like timer is “Upon reception of the RRCReconfiguration message including sl-IndirectPathAddChange”.
[Easy]Proposal 19: [15/19] The remote UE falls back to the configuration/operation prior to indirect path addition/change at the expiry of new T420-like timer. FFS whether/how to handle the path change case that the prior indirect path is released before the T420 expiry.
[Easy]Proposal 20: [15/19] The remote UE reports the failure of indirect path addition/change to gNB at the expiry of T420-new like timer. FFS whether this is conditional on the available of SRB1 in direct path.
[Easy]Proposal 22: [14/19] The remote UE may not initiate RRC reestablishment procedure upon the expiry of new T420-like timer. FFS whether this is conditional on the availability of SRB1 in direct path.
[Easy]Proposal 23: [19/19] For path addition/change cases in MP Scenario 1, RRCReconfgurationComplete is always transmitted in direct path. Only if NW configures split SRB1 with PDCP duplication, RRCReconfigurationComplete message is sent to gNB via both paths.

## Slide 16: Annex: Remaining Proposals in R2-2310350
[To discuss]Proposal 4: [13/20] Not support the remote UE reporting the failure of direct path addition/change to the gNB at the expiry of T304 timer.
[To discuss]Proposal 6: Upon T304 expiry, RAN2 to discuss whether RRC establishment is always triggered w/o any condition (11/18) or only when SRB1 in indirect path not configured/suspended (7/18).
[To discuss]Proposal 8: [10/20] RAN2 to discuss whether/how to avoid/handle the case when the target L2 MP Relay UE establishes a RRC connection with a different gNB than the gNB serving the target cell.
[To discuss]Proposal 9: [10/10] If the error case in P8 is to be addressed, remote UE reports the “wrong gNB” failure to PCell after the failure is detected. FFS how remote UE detects this failure (e.g., differentiate this case with the case that relay UE reselects another cell under the same gNB).
[To discuss]Proposal 13: [9/13] Rely on NW indication to remote UE whether PC5-RRC trigger is used or not. FFS whether this indication can be relay UE RRC state.
[To discuss]Proposal 16: [10/20] The T420-like timer stop condition of IDLE/INACTIVE relay case depends on whether RRCReconfguraitonComplete is sent via indirect path or not, assuming legacy Rel-17 T420 condition can be reused if yes.
[To discuss]Proposal 17: [13/20] Dowon-select one of the following for the T420-like timer stop condition of IDLE/INACTIVE relay addition/change (at least for the case that RRCReconfguraitonComplete is not sent via indirect path):
- Option 1: upon PC5-RRC connection establishment
- Option 2: Upon PC5 RLC acknowledgement of the PC5-RRC message triggering relay UE entering CONNECTED state
- Option 3: upon reception of RRCReconfigurationCompleteSidelink
[To discuss]Proposal 18: RAN2 to discuss whether the T420-like timer stop condition of CONNECTED relay case is as same as legacy Rel-17 T420 stop condition (11/20) or same as condition(s) in IDLE/INACTIVE case, if applicable.
[To discuss]Proposal 21: [10/15] If indirect path add/change failure is to be reported, include the indication of failure and the reason causing the indirect path failure in the report (assuming indirect path failure is implicitly or explicitly indicated by the report message) .

## Slide 17: Proposal 3 in R2-2310781
Proposal 3: RAN2 discusses whether Rel-17 Relay UEs can be considered as candidate target Relay UEs.
Proposal 4: Relay UE indicates whether to 1) support and 2) need PC5-RRC triggering in discovery message (i.e. AS container). Send LS to SA2 and CT1.
Proposal 5: If only Rel-18 Relay UEs are considered as candidate target Relay UEs, then the Remote UE only reports Rel-18 candidate Relay UEs to the gNB;
Proposal 6: If both of Rel-17 and Rel-18 Relay UEs are considered, the Remote UE indicates Relay UE’s release info or whether support PC5-RRC triggering to the gNB.