## Slide 1: Summary of Offline -103 IUC MAC CE in Rel-18 SL Evo
Apple (Rapporteur)
R2-2401784

## Slide 2: Background
[AT125][103][V2X/SL] IUC Enhancement (Apple)
Scope: Check RAN1 status, discuss and determine IUC Enhancement format, field description (if needed), and need of separate (e)LCID reservation.
Intended outcome: Discussion summary in R2-2401784 and TP in R2-2401785
Deadline: Comeback in CB session (2/29)
Papers involved
  R2-2300232 (OPPO)
  R2-2300270 (Sharp)
  R2-2300962 (LG)
  R2-2300946 (Apple)
Confirm the common understanding as follow:
  New IUC-Req and IUC-info MAC CE formats are needed to be aligned with RAN1’s new SCI format in R18 for SL-U.
  New field “Lowest RB set index” is needed in IUC-Info. Size is 3-bit.
  New field “Number of RB set” is needed in IUC-Req. Size is 3-bit
  Size of “RC” field in New IUC-info MAC CE is changed to 28-bits.

## Slide 3: Discussion [1]
Issue 1: Both legacy formats and new formats are needed in R18 MAC Spec?
  [Rapp] Which format is a Rel-18 UE is to use to send IUC-Request/Info to Rel-17 UE
  [OPPP]: Based on RRC configuration, both formats are needed for R18 UE: [Rapporteur]: we have the same view]
  Proposal 1: Both legacy format and new format of IUC MAC CEs are included in R18 spec.
Issue 2: new LCIDs needed?
  [Rapp] Is per-pool RRC parameter “sl-TransmissionStructureForPSCCHandPSSCH” “not configured or configured as “contigousRB “ vs. “InterlaceRB” is sufficient for UE to determine the format to use?
  [ZTE] logically, it can work w/o introducing new LCID, but it is safe to follow legacy practice to add new LCID for every new MAC CE format. Xiaomi: the length of MAC CE is different. Prefer to use new LCID in MAC subheader. Also, LCID space is large enough to add two more. [Nokia, Sharp, Samsung]: Agree with ZTE and Xiaomi. [Rapp] We can follow majority view.
  Proposal 2: new LCIDs in SL interface are introduced for new IUC MAC CEs.

## Slide 4: Discussion [2]
Issue 3: Is there a need to reduce the size of “number of subchannels” (existing R17 field) from 5 bits to 4 bits:
  Do we need further RAN1 input, or can just go with 5-bit (safe choice)?
  [Apple, OPPO]: Our RAN1 delegates confirms that only 4-bits are needed.
  Proposal 3: The “number of subchannels” field and LSI in IUC MAC CEs are 4-bit field.
Issue 4: whether the new LRI (“Lowest RB set Index”) field in front or behind the corresponding “RC” field in IUC-info MAC CE?
  [OPPO] This can be left to MAC rapporteur to decide.
  No proposal is needed for this issue.

## Slide 5: Conclusion
Proposal 1: Both legacy format and new format of IUC MAC CEs are included in R18 spec.
Proposal 2: new LCIDs in SL interface are introduced for new IUC MAC CEs.
Proposal 3: The “number of subchannels” field and LSI in IUC MAC CEs are 4-bit field.