## Slide 1: Outcome of A-IoT forward compatibility offline
Huawei, HiSilicon
3GPP TSG-RAN WG2 Meeting #131
Bengaluru, India, 25-29 August 2025
R2-2506441

## Slide 2
Forward compatibility
  “Critical extension”: Add a 1-bit version field in paging message, Msg2, NACK feedback message, R2D upper layer data transfer message, and Rel-19 devices drop the whole message when version field is set to 1. When set to 0, it will parse the message according to Rel-19 specification. [CB] for trigger access
  “Non-critical extension”: At least paging message can be extended to add more fields at the end of the message in further releases, and Rel-19 devices ignore the extension parts added in future release instead of dropping the whole message. [CB] whether explicit R bit is needed for the purpose of this extension and if applicable to other R2D message and access trigger
  Non-critical extension:
    Point-1: For paging message, there is no need of explicitly “R/Extension” bit for this “Non-critical extension” in R19?
      Rapp: No need
    Point-2: In addition to paging, any other R2D message needs to this “Non-critical extension”, e.g. Access Trigger message?
      Rapp: No need of any other R2D message
  Critical extension:
    Point-3: Do we need this 1-bit version field?
    Option 1: use message type to achieve critical extension without version field (both are fine: )
      Option 1-1: Use 3-bit R2D message type. Use reserves values first if overhead is prioritized. Can use a reserved value as future indication like eLCID, if needed. (Xiaomi, Huawei, ZTE, DCM, Ericsson, Lenovo, IDC, MTK, ETRI, Vivo)
      Option 1-2: Use 4-bit R2D message type; [Use 3-bit R2D message type for access trigger (0010 and 0011)] (Apple, SS, LG, QC, Nokia)
    Option 2: introduce this 1-bit version field; (No: IDC, QC, Xiaomi, Apple)
    Point-4: If go with version bit in option 2, do we apply it to Access Trigger message?
Conclusion: Suggest to use the following proposals to replace the online agreements for forward compatibility:
Proposal 1: Paging message can be extended to add more fields at the end of the message in further releases, and Rel-19 devices ignore the extension parts added in future release instead of dropping the whole message, without extension indication. Future extension using the same message type is not supported for R2D messages other than paging message.
Proposal 2a: Do not introduce 1-bit version field (i.e., Rel-19 devices drop the whole message when version field is set to 1. When set to 0, it will parse the message according to Rel-19 specification). Remove the R-field in paging message from the running CR.
Proposal 2b: FFS if to extend 3-bit R2D message type to 4 bits:
Option 1-1: Use 3-bit R2D message type. Use reserve values first if overhead is more critical. Can use a reserved value as future indication like eLCID, if needed. (Xiaomi, Huawei, ZTE, DCM, Ericsson, Lenovo, IDC, MTK, ETRI, vivo)
Option 1-2: Use 4-bit R2D message type. (Apple, SS, LG, QC, Nokia)

## Slide 3
Annex
Figures of related MAC PDU formats and message type table

## Slide 4
Without explicit “R bit/Extension indication” as captured in current CR
With explicit “R bit/Extension indication”

## Slide 5
Access Trigger message
Msg2
NACK Feedback message

## Slide 6
R2D Data Transfer message
R2D Message Type value | R2D message name
000 | Reserved
001 | A-IoT Paging message
010 | Access Trigger message
011 | Random ID Response message
100 | R2D Upper Layer Data Transfer message
101 | NACK Feedback message
110 | Reserved
111 | Reserved
Table 6.1-1: R2D Message Type as in current CR

## Slide 7
R2D Message Type value | R2D message name
0000 | Reserved
0001 | A-IoT Paging message
0010 | Access Trigger message
0011 | Random ID Response message
0100 | R2D Upper Layer Data Transfer message
0101 | NACK Feedback message
0110-1111 | Reserved
  Option 2a: Use 4-bit R2D message type;
R2D Message Type value | R2D message name
0000 | Reserved
0001 | A-IoT Paging message
001x (x=0 or 1) | Access Trigger message
0100 | Random ID Response message
0101 | R2D Upper Layer Data Transfer message
0110 | NACK Feedback message
0111-1111 | Reserved
  Option 2b: Use 3-bit R2D message type for access trigger (0010 and 0011) and 4-bits R2D message type for other R2D messages;