## Slide 1: Work Item Proposal for User Plane Congestion Management (UPCON)
NEC, ...
3GPP TSG RAN2#83,
Barcelona, Spain, 19-23 August 2013
R2-132689

## Slide 2: Current scope of UPCON WI in SA2
The SA2 objectives of the UPCON WI are as follows:
  As part of the TR phase, define the architectural requirements (based on the SA1 normative requirements) in order to scope/guide the work;
  Develop solutions for user plane congestion mitigation based on objective 1; and
  Determine which solution(s) from the TR phase to document in normative specifications, and specify them accordingly.
Due to limited time budget in Rel-12, prioritization of features is required .
The latest TR 23.705 V0.6.0 can be found at http://www.3gpp.org/ftp/tsg_sa/WG2_Arch/Latest_SA2_Specs/Latest_draft_S2_Specs/23705-060.zip

## Slide 3
UPCON feature component and dependency analysis (based on SP-130335)
(NOTE: Red text indicates RAN dependency; red arrow indicates some solutions for the feature may have RAN dependency)
(I) Service/best effort UP prioritization
(D) RAN Congestion Reporting
(G) Content specific UP prioritization (Video)
(H) App specific UP prioritization
(ext1) RAN feedback on solutions with RAN impact
(C) RAN Congestion Detection
(B) Uplink Congestion Management
(F) CN Congestion Mitigation with dynamic PCC control, per subscriber policies
(A) RAN Traffic Differentiation
(E) Dynamic PCC control, Per Subscriber Policies
Includes traffic differentiation enhancements (e.g. marking, priority, etc.) and considerations for shared networks.
Identification, differentiating and prioritization of uplink traffic, either by per-flow or per user (e.g. depending on subscription characteristics) policies.
Determine if the RAN is congested. This includes considerations of ‘what’ congestion is, ‘when’ (to distinguish between transient and sufficiently long periods to take action, e.g. to report congestion.)
(G) Includes handling of video streams more efficiently either for RAN-based solutions.
(H) Includes how App specific UP prioritization works in the RAN and standardized identification of applications.
(I) Includes discriminating between attended and unattended data traffic.

## Slide 4: Summary of core specification work in working groups
Impacts to RAN2:
  Description of detection of RAN user plane congestion levels based on RAN measurements (C)
  Develop solutions for the following features:
    RAN DL traffic prioritization based on packet markings in CN (A)
    Uplink congestion management, including uplink traffic prioritization (C)
    Depending on the SA2 outcome, potentially for video, app, and un/attended traffic (G), (H), (i)
Impacts to RAN3:
  Specification/indication of RAN user plane congestion levels (A)
  Potential impacts on RAN interfaces (all features with RAN impact)

## Slide 5
Estimated RAN Work Load for all feature components
(not prioritized)
Features | Open Issue | RAN2 | RAN3
(A) RAN Traffic Differentiation | Intra-bearer DL traffic prioritization based on packet markings. May impact Uu protocol stack and eNB interfaces. NOTE: DL is deemed more pressing than UL due to observed traffic statistics. | 3 TU | 2 TU
(B) Uplink Congestion Management | Inter- and intra-bearer UL traffic differentiation | 4 TU | 1 TU
(C) RAN Congestion Detection | Implementation-independent, configurable congestion detection (also see SA2 LS to RAN2 and RAN3 / R2-132280 = R3-131207). Without congestion detection, CN control of mitigation is not possible. | 1 TU | 2 TU
(G) Content specific UP prioritization (Video) | More efficient handling of video streams for RAN-based solutions. NOTE: in SA2, there was no solution proposed yet with RAN dependency. | ? | ?
(H) App specific UP prioritization | App specific UP prioritization in the RAN . NOTE: in SA2, there was no solution proposed yet with RAN dependency. | ? | ?
(I) Un/Attended UE Information | Discrimination in RAN between attended and unattended traffic. | 3 TU | 1 TU
Total |  | >= 11 TU | >= 6 TU
(NOTE: The numbers are estimates for work in E-UTRA. Additional work may be necessary for UMTS, GERAN).
TU = Time Unit

## Slide 6: Proposed Way Forward
PROPOSAL: Approve new RAN3-led UPCON work item in RAN to do the normative work necessary to support SA2.
Following the operators' request in RP-13xxxx, the following priorities for work in E-UTRA in Rel-12 are proposed and documented in the WID:
  Priority 1:
    Congestion detection (C). Without congestion detection and indication, CN control of mitigation is not possible.
  Priority 2:
    DL RAN traffic differentiation (A). DL is deemed more pressing than UL due to observed traffic statistics.
  Priority 3:
    Uplink congestion management, and all other features with RAN dependencies. RAN2 is too busy to spend the required >= 7 TU.