## Slide 1: Discussions on Type 2 PHR
Intel
3GPP TSG RAN WG2 Meeting #90
Fukuoka, Japan, May 25th – 29th, 2015
Agenda Item: 6.1.2
R2-152787

## Slide 2: Discussion 1
---- <Text in section 5.4.6. of TS 36.321>------------
- if simultaneousPUCCH-PUSCH is configured:
- obtain the value of the Type 2 power headroom for the PCell;
- if the MAC entity has a PUCCH transmission in this TTI:
obtain the value for the corresponding PCMAX,c field from the physical layer;
---------------------<End text citation>------------------
According to text heighted above in current spec , MAC entity is required to know whether a PUCCH is transmitted or not in the reporting TTI.
This should be relaxed according to RAN1 LS!!!!!!!

## Slide 3: RAN1 LS
=====<Citation text in RAN1 LS reply R2-152006 >=====
RAN1 would like to inform RAN2 that RAN1 discussed this issue and agreed that:
If both PUCCH format 1b with channel selection and simultaneousPUCCH-PUSCH are configured, in some cases, UE may not be able to determine whether there is a PUCCH transmission corresponding to PDSCH transmission(s) or not, or which PUCCH resource is used, before generating Type 2 PH, upon (E)PDCCH detection.
  It is necessary to relax UE processing time requirement with these conditions.
    UE is allowed to report virtual PH with these conditions.
    If UE is able to determine there is a PUCCH transmission and which PUCCH resource is used before generating Type 2 PH, UE shall report the actual PHR.

## Slide 4: Discussion 2
RAN1 specification does not describe any procedure. Therefore, RAN1 spec is not suitable place to capture this agreement. That is why RAN1 recommended specifically to add in “Our specification” in the RAN1 LS.

## Slide 5: Way forwards
WF1: Agree R2-152211.
WF2: Capture the RAN1 agreements into RAN1 and RAN2 spec separately.
  Agree the text proposal in next slide.
  Send LS to RAN1 to ask them for specification changes.

## Slide 6: Details of WF2
NOTE: The MAC entity is allowed to not obtain PCMAX,c field if following conditions are met:
  - if both PUCCH format 1b with channel selection (see TS 36.213 [2]) and simultaneousPUCCH-PUSCH are configured, and
  - the MAC entity is not able to determine whether there is a PUCCH transmission corresponding to PDSCH transmission(s) or not, or which PUCCH resource is used, before generating power headroom.
Changes on TS 36.321
The PHY entity is allowed to report Type 2 power headroom based on a PUCCH reference format, if following conditions are met:
  if both PUCCH format 1b with channel selection (see TS 36.213 [2]) and simultaneousPUCCH-PUSCH are configured, and
  the PHY entity is not able to determine whether there is a PUCCH transmission corresponding to PDSCH transmission(s) or not, or which PUCCH resource is used, before generating power headroom.
Changes on TS 36.213