## Slide 1: Wayforward on suspended MTCH
ZTE, Ericsson, Huawei, CATT, Qualcomm, NEC

## Slide 2: Legacy MSI
While MTCH is not scheduled and not suspended, the “LCID” is listed/not listed in the MSI and the value of “Stop MTCH” is set to 2047 (if listed)?(listed: NN, ZTE, QC, CATT, Samsung, HW, Ericsson, NEC) Note: The discussion is related to the case when there is data for transmission for at least one MTCH in this MCH.
While MTCH is suspended, the “LCID” is listed/not listed in MCCH? (not listed: ZTE, NN, HW, LGE, QC, CATT, Samsung, Ericsson, NEC) Note: MTCH is removed at the next modification period.
While MTCH is suspended, the “LCID” is listed/not listed in the MSI and the value of “Stop MTCH” is set to 2047 (if listed)? (not listed: ZTE, NN, HW, LGE, QC, CATT, Samsung, Ericsson, NEC)

## Slide 3: Extended MSI
Extended MSI with S field is used only if a MTCH is to be suspended. Otherwise, the Extended MSI without S field is used.? (Yes: NN, ZTE, QC, CATT, Samsung, HW, NEC) Note: The format of the Extended MSI without S field is the same as the legacy MSI.
If MTCH is to be suspended, the “LCID” is listed in the extended MSI and the value of “S” field is set to “000” (if listed)? (Yes: NN, ZTE, QC, CATT, Samsung, HW, NEC)

## Slide 4: L field of MCH MAC subheader
Zero value of the L field in MAC subheader is invalid for MCH MAC PDU? (invalid: HW, NN, ZTE, CATT, Samsung, Ericsson, NEC; valid: LGE)
Zero value of the L field in MAC subheader is invalid for DL-SCH MAC PDU? (invalid: NN, Samsung, HW; valid: LGE)

## Slide 5: Conclusion
Note: The following conclusions are only to confirm RAN2 understandings. Whether CRs are needed is FFS.
Conclusion 1: While a MTCH is not scheduled and not suspended, the “LCID” is listed in the MSI and the value of “Stop MTCH” is set to 2047.
Conclusion 2: While a MTCH is suspended, the “LCID” is not listed in MCCH.
Conclusion 3: While a MTCH is suspended, the “LCID” is not listed in the MSI.
Conclusion 4: Extended MSI with S field is used only if a MTCH is to be suspended. Otherwise, the Extended MSI without S field is used.
Conclusion 5: While a MTCH is to be suspended, the “LCID” is listed in the extended MSI and the value of “S” field is set to “000”.
Conclusion 6: Zero value of the L field in MAC subheader is invalid for MCH MAC PDU.