## Slide 1: Way forward for NAS timer setting
Ericsson
3GPP TSG-RAN WG2 Meeting #93bis R2-162996 Dubrovnik, Malta, 11 – 15 April 2016

## Slide 2: Background (1)
Agreements:
1 NAS should be aware that a UE only capable of CE mode A. RAN2 understanding is that legacy timers would be suitable.
Tentative agreements:
2 For a UE that supports CE mode A and CE mode B: Two levels of CE information will be provided to NAS. 1/ UE in NC or CE mode A. 2/ UE in CE mode B
2a On UE side the NAS can be informed by UE internal signalling at connection establishment.
FFS when exactly during the connection establishment the CE information will be available in UE.
2b On network side, the CE information should be provided in the S1 message carrying Initial NAS message
3 Ask CT1 if it is useful for NAS to be informed during an RRC connection that the CE mode has been reconfigured.
=> The tentative agreements can be discussed mode offline (Ericsson)

## Slide 3: Background (2)
Triggered by SA2 LS
R2-162119 Reply LS to R3-160135 = R2-161014 on questions on NB-IoT (S2-161333; contact: Vodafone) SA2 LS in to: RAN2 Rel-13 NB_IoT-Core, CIoT
RAN3 is studying how to convey a ”NAS PDU Transmission Delay Indicator” (a multiplication factor), from eNB to MME at INITIAL UE MESSAGE (and RRC Resume), based on the CE level used at RRC Connection establishment (resume)
Draft CR to S1AP is being discussed by RAN3
Does not cover UE side.

## Slide 4: Proposal
UE Side
  Similar solution for eMTC and NB-IoT
  Solution needed for UE that support CE mode B (and NB-IOT UE)
    Introduce new IE to convey a ”NAS transmission delay indicator” (multiplication factor) in RRC signalling when CE mode (level) is signalled to UE.
      For eMTC CE Mode B , potentially agree on default value used by UE
    Initial value at RACH (for e.g. SERVICE REQUEST) depends on UE CE Level.
      Value of ”NAS transmission delay indicator” to use by UE is FFS.
    CR to 36.331 can be produced for next meeting

## Slide 5: Proposal
Nw side
  Use RAN3 solution for S1AP signalling
    ”NAS PDU Transmission Delay Indicator” (a multiplication factor) from eNB to MME at INITIAL UE MESSAGE (and RRC Resume).
    Would result in that NAS timer setting is not modified during ongoing long-duration RRC connection in case CE mode changes.
      Could be acceptable solution for Rel-13, no need to check with CT1.