## Slide 1: Anchor to non-anchor switch after RACH in RRC Connected
RAN 2#94 preparation and planning

## Slide 2: Switching from Anchor to Non-anchor after RACH in RRC Connected

## Slide 3: Switching from Anchor to Non-anchor after RACH in RRC Connected
  Same flowchart for UE initiated case (without PDCCH order)
  The following text is extracted from TS36.321:
  Based on the above:
    UE initiated case:
      Alt1: UL grant provided in Msg4 is for anchor carrier but UE ignores the UL grant and starts monitoring the PDCCH of the non-anchor carrier after receiving Msg4.
      Alt 2: UL grant provided in Msg4 is for the non-anchor carrier and UE will apply the UL grant on the non-anchor carrier after receiving Msg4.
    eNB initiated case (with PDCCH order):
      Alt1: UL/DL grant provided in Msg4 is for anchor carrier but UE ignore the UL/DL grant and start monitoring the PDCCH of the non-anchor carrier after receiving Msg4.
      Alt 2: DL/UL grant provided in Msg4 is for the non-anchor carrier and UE will apply the DL/UL grant on the non-anchor carrier after receiving Msg4.

## Slide 4: Alternative 3 (from Neul)
Alternative 3:
UE switch to monitoring non-anchor carrier after first transmission of Msg3
Msg4 (contention resolution) is received from Non-anchor carrier

## Slide 5: Quick comparison
  Alt 2: Require cross-carrier scheduling (i.e. anchor carrier providing UL grant for non-anchor carrier in Msg4)
  Alt 3: Seems to result in HARQ retransmission of Msg3 in non-anchor carrier (HARQ combining in anchor and non-anchor carrier)