## Slide 1: Way Forward for Change notification of SC-MCCH (For UEs interested in the new Session Start)
Huawei, Hisilicon, Intel, ZTE, Qualcomm, Sequans, CATT, …

## Slide 2: Background
Current mechanism:
  Change of SC-MCCH is notified in a specific/dedicated PDCCH scrambled by SC-N-RNTI.
Motivation for enhancement:
Both power efficiency and resource efficiency will decrease significantly for UEs to monitor a specific PDCCH.

## Slide 3: Potential solutions
Solutions:
  Option 1: Use 1 bit in the DCI in PDCCH for SC-MCCH scheduling
  Option 2: Use 1bit in DCI in Direct Indication
Proposal:
  Option 1: Use 1 bit in the DCI in PDCCH for SC-MCCH scheduling, and SC-RNTI is used.