## Slide 1: Way Forward for Change notification of SC-MCCH (For UEs with on-going service)
Huawei, Hisilicon, ZTE, …

## Slide 2: Background
Problem for current mechanism:
  The SC-MTCH for the UE who has on-going service will be interrupted by SC-MCCH reception at each MP
Motivation for enhancement:
To avoid the above problem
Benefit for the performance of SC-MTCH to save UE power

## Slide 3: Potential solutions
Proposal 1: Use 1 bit in DCI in NPDCCH for SC-MTCH scheduling to indicate whether the configuration of the SC-MTCH will be changed in next MP.
Proposal 2: Use 1 bit in DCI in NPDCCH for SC-MTCH scheduling to indicate whether the new services are due to start in next MP.
  For the UE who has on-going service and is interested in detection of other new session starts.