## Slide 1: Compromise Solution
Explanation of Key Properties
-
Addressing the concerns raised in R2-169092

## Slide 2: TX Pre-Processing Compromise Proposal
Pre-processing: PDCP ciphering, addition of PDCP headers and interleaved Length Fields
On-the-fly computation for each TB (sequentially):
  Determine the number of pre-computed octets per TB:
    nrofPayloadOctets = min(TBSize, dataInLCH) – MacHeaderSize – RlcHeaderSize (header sizes are fixed)
  Determine memory position of the corresponding first data octet per TB
  Stream pre-generated data to the L1 encoders for all TBs
Significant simplification on-the-fly computation compared to LTE  Considered feasible in very few CPU cycles even for multiple TBs

## Slide 3: TX Pre-Processing ”No-Concatenation”
“No Concatenation” solution does not only enable pre-processing but it rather requires pre-generating RLC PDU headers since it is not feasible to generate hundreds of RLC headers on the fly.
However, RLC SNs & poll bits cannot be pre-determined reliably (due to PDU Discard and Split bearer)  requires “late pre-processing”  additional (double) memory accesses  significantly higher processing load  significantly lower throughput/capacity with same hardware.

## Slide 4: TX Pre-Processing ”No Concatenation”
Parallel TX: Based on offline explanations, the transmitter is expected to interleave subsequent PDCP/RLC/MAC PDUs across the Transport Blocks  Leads to massive re-ordering at RLC RX side and defeats the original idea to stream sequentially from pre-processed data stream
1
2
3
4
5
6
7
8
…
1
3
2
4
5
6
7
TB1
TB2
TB3

## Slide 5: RX Processing Compromise Proposal
Control information (MAC sub-headers, MAC CEs) at a known position  Accelerates extraction of the urgent control information and dispatching subsequent (RLC, PDCP) processing
One or a few (large) RLC PDUs per TB  Minimizes ARQ processing
The PDCP PDUs within the RLC PDU payload are in the correct order  minimizes re-ordering on the RX side
Note: Both solutions assume currently that MAC CEs (BSR, PHR) can only be provided in the end of the transport block due to TX side time constraints.

## Slide 6: RX Processing “No Concatenation”
The interleaving PDCP PDUs across parallel transport blocks at the TX side (see above) makes receiver side processing load unpredictable
  Previously it was argued that all RLC SNs are in sequence and that the ARQ processing effort remains therefore low.  If the “no concatenation” solution requires interleaved PDCP PDU transmission, this argument does not hold anymore.

## Slide 7: Overhead
In general and including the case where two (or more) VoIP packets are bundled into one TB, the compromise solution has the same or lower overhead.
Only in case where one VoIP packet fits exactly into one transport block the compromise solution has higher overhead (2 byte per TB). However, the delay based scheduling results in VoIP frame bundling as soon as all resources are utilized, i.e., when overhead matters… and then the solutions have the same overhead.
  Note: Due to flexible TTI duration, the VoIP frame bundling will be possible even for UEs in bad coverage conditions

## Slide 8: Specification Impact Compromise Proposal
Interface between PDCP & RLC
  As in LTE, PDCP delivers PDCP PDUs to RLC.
  RLC TX prepends each SDU with a Length Field which the RLC RX uses to extract and reassemble the RLC SDUs.
  RLC RX delivery the PDCP PDU to PDCP  Clean interface
Maturity of “Compromise Proposal”
  Proposal to interleave Length Fields while maintaining concatenation has already been presented by DCM prior to RAN2-95bis.
  PDCP/RLC/MAC protocol logic follows exactly the same principles as LTE
  Only the header formats are adjusted to accelerate TX side processing
  Note: “No-Concatenation” solution changes protocol logic compared to LTE (mapping of PDCP PDUs to RLC and MAC PDUs; principle of minimizing the RLC PDUs and SNs per MAC PDU, …). Proponents suggest several enhancements and fixes to be considered later.

## Slide 9: Architecture Impact
As stated during this week, the Radio Interface protocol should be optimized for the radio interface and not for the transport network
It should be noted that the proposed compromise protocol stack could be applied to RAN3’s protocol architecture alternative 3.1 (Split RLC), similar to “No Concatenation” approach
  However, it would suffer from the same problems that we observe for the “no concatenation” (increased ARQ processing, problems with PDU Discard, …)