## Slide 1: Way forward on Release Assistance Information (RAI) in NB-IoT
Ericsson, Docomo
R2-1702262
TSG RAN WG2 meeting #97
13-17 Frebruary 2017, Athens

## Slide 2: Proposed way forward
Baseline in:
R2-1701048(CR 36.306):
  Optional UE capability
R2-1701049 (CR 36.321):
  BSR=0 indicates that UE does not have more data to send/receive in near future
  Timer handling:
    When rai-ProhibitTimer is configured and BSR=0 is sent rai-ProhibitTimer is started
    When rai-ProhibitTimer is configured and running BSR=0 is not sent
R2-1701050 (CR 36.331):
  rai-ProhibitTimer included in IE MAC-MainConfig-NB
  Value range (s0, s5, s10, s20, s30, s60, s90, s120)

## Slide 3: Proposed way forward
Potential corrections/improvements:
  Clarify in 36.321 that UE shall keep rai-ProhibitTimer in Idle-Connected mode transitions
  Correct in 36.331 rai-ProhibitTimer to Need OR, i.e. RAI procedure is stopped when timer is omitted