## Slide 1: WF on power consumption reduction for NB-IoT
Veolia
3GPP TSG-RAN WG2 Meeting #99
Berlin, Germany, 21 – 25 Aug 2017
Agenda item: 9.13
R2-1709543

## Slide 2: Background (1/2)
For IoT, power consumption saving is paramount.
It is even more critical for use cases with stationary UEs that are battery powered and are subject to long term contracts (such as Smart Water Meters).
Even a small saving could make the difference between being able to have battery life time of those UEs adapted to those contracts or not.
These use cases are also characterised by one UL small data transmission sent at a regular large interval and a state in Idle/PSM mode in between each UL transmission (see [2]).
Existing LTE procedures entail significant overhead that could be drastically reduced specifically for those use cases with periodic UL small data transmission.

## Slide 3: Background (2/2)
One of the objectives of the WI “Further NB-IoT enhancements” (see [1]) is to provide further latency and power consumption reduction.
Several overhead reduction Enhancements are particularly beneficial for the use cases mentioned before:
  Enhancements with little impacts on the specification:
    Quick RRC Connection Release: there is a delay of 10s after the UE has received the RRC Connection release message which could be removed
    Relaxed monitoring for cell reselection (see [3])
  Enhancements with big impacts on the specification but potentially huge savings:
    Early UL Data transmission – Eliminate the Msg5 by adding the NAS PDU in Msg3 for small UL data transmission
    SPS: potential to reduce the RACH procedure through dedicated IoT SPS

## Slide 4: Proposals
Quick RRC Connection Release: Remove the need for a timer of 10s by going to idle as soon as HARQ-ACK has been sent by the UE as part of TEI14.
Introduce relaxed monitoring for cell reselection for stationary UEs as part of TEI14.
Specify early data transmission solution which has lower overhead and power consumption considering the actual payload sizes and requirements described in [2].
Specify a dedicated IoT SPS for stationary UEs different than the LTE SPS working when the UE is in idle/PSM mode and allowing large SPS period (for example 12 hours).

## Slide 5: References
[1] | RP-171428 | New WID on Further NB-IoT enhancements | Huawei, Hi-Silicon
[2] | R2-1708447 | UL small data transmission use cases and requirements | Veolia
[3] | R2-1708277 | [98#52][NB-IoT] Power Consumption for RRM | Ericsson