3GPP TSG-RAN WG3#107-e                                             	                     R3-201245

E-Meeting, 24th February – 6th March 2020

Agenda item:	9.3.8.1

Source:	Nokia, Nokia Shanghai Bell

Title: 	Summary of offline discussion on DC Operation Correction (CB104)

Document for:	Approval

# 1   Introduction

This is the summary of the following email discussion:

9.3.8 Others – DC Operation correction

| R3-200149 | Correction of DC Operation Mode (Nokia, Nokia Shanghai Bell, Orange) | discussion discuss how to inform AMF when an NG-RAN node operates in NSA mode only sol1: OAM sol2: indication in NG setup req sol3: trial/error: “NG-RAN node is restricted to operate in NSA mode only” (e.g. cause value) proposed CRs cover sol2 noted SS: SA-only and NSA-only are possible? Nok: yes, in which case no need for NG interface HW: sol1 should not be ruled out CATT: should not just “reject” UE Nok: good question, hence the need for a solution; pure sol1 does not work, because it defeats the purpose of ANR CB: # 104_DCoperationCorrection - clarify scenario - sol1 seems to negate ANR? - is sol3 acceptable? Seems Trial/error only once per NG-RAN node? - revise CRs if needed (Nok) Summary of offline disc R3-201245 |
| --- | --- | --- |

# 2   Description

Nokia explained that the issue is a follow-up on the discussion of last RAN3#106 where RAN3 concluded that NG-RAN nodes which work in SN-only mode shall still connect to AMF. The issue addressed at this RAN3#107 meeting is consequently how can AMF handle such nodes if it is not aware that they are SN-only?

During the online discussion, one company said we cannot exclude O&M solution 1.

Nokia explained that O&M puts the burden on operator’s back and is anyway not a good solution: this is because relying on O&M only means that the operator has to configure in advance which NG-RAN nodes will connect to an AMF in future working in SN-only mode. Therefore, the operator needs to feed the AMF(s) in advance with the NG-RAN nodes IDs or IP addresses of these NG-RAN nodes which will connect. This defeats the purpose of SON/ANR where NG self-configuration (NG setup) is based on bottom-up approach where the NG-RAN node is configured with the IP addresses of the AMF to connect to, and not the other way round.

Another company suggested to use solution 3 with specific cause value. It was clarified that in this solution 3 the AMF would learn in a kind of try and failure mode. This was not excluded.

The position of companies was captured below:

Question 1: which solution do you prefer between solution 1 (O&M), solution 2 (NG setup) solution 3 (try and failure)?

| Company | answer | Detailed answer |
| --- | --- | --- |
| Nokia | Solution 2 | Seems the cleanest solution. This respects the basic SON dynamic setup principle and allows automatic updates when configurations change. This also offers better longer-term solution and is less prone to errors. |

# 3   Conclusion and proposal

Proposal: .

# 4  References

- RP-172109, Revised Work Item on New Radio (NR) Access Technology, NTT DOCOMO, Inc.

- 3GPP TS 23.501, Architecture for Next Generation System, SA2